TRAIN POSITION
Véronique Gontier
Munich 06/14

---
TRAIN POSITION INFORMATION
The Train Position information defines the position of the train front in relation to a balise group, which is called LRBG (the Last Relevant Balise Group). It includes:
* The estimated train front end position, defined by the estimated distance between the LRBG and the front end of the train
* The train position confidence interval
* Directional train position information in reference to the balise group orientation of the LRBG, regarding:
     - the position of the train front end (nominal or reverse side of the LRBG)
     - the train orientation
     - the train running direction
* A list of LRBGs, which may alternatively be used by trackside for referencing location dependent information
(SRS.3.6.1.3)

---
DIRECTIONAL TRAIN POSITION INFORMATION (1/2)
Running Direction
Active Cab
1 2 3 4
=
4 3 2 1
=
Front end
Rear end
BG orientation
Balise antenna
Running Direction = normal
LRBG
LRBG
Running Direction = reverse
Train Direction = normal
LRBG
LRBG
Train Direction = reverse

---
DIRECTIONAL TRAIN POSITION INFORMATION (2/2)
Train position = normal
LRBG
LRBG
Train position = reverse

---
ODOMETRY DEFINITIONS (1/2)
max
Start
estimated
Confidence interval
0
min
Max, estimated and min values are given by odometry
The confidence interval shall be < 5 %
Odometry calculates these values each 100ms (about)
N.B.: the confidence interval always increases as the train moves, forward OR
backward
d-ant
d-ant = distance between the front end and the balise antenna (about 3m)

---
ODOMETRY DEFINITIONS (2/2)
0 Odo 2
0 Odo 1
Start
Cab 2 = non active
Cab 1 = active
Odo 2 : increase
        decrease
Odo 1 : increase
        decrease
Generally, a train has two OBU and two odometries, one for each cab
Only one cab is active but the two odometries always work : one increases and the other decreases. So, if the active cab changes, the location is preserved and the reference (0 odo) automatically changes

---
SIMPLIFIED LOCALISATION
To localize a train,two data are needed:
- LRBG (Last Relevant Balise Group), whose localisation is known
- d-FrontEnd: distance between the train front end and the LRBG
  This value is calculated with odometry information
d-FrontEnd
LRBG
0
n
d-ant
LRBG odometry distance
n odometry distance
d-FrontEnd = n odometry distance – LRBG odometry distance + d-ant
NB : if the train goes backward, this value can be negative
d-FrontEnd
LRBG

---
TIME CYCLE CORRECTION
The OBU cycle is about 300ms and the odometry one is about 100ms
A timer distributes the same time to the OBU, the odometry and balise antenna system
together
At its cycle beginning, the OBU asks odometry a set of refreshed data to calculate
the FrontEnd position, and the odometry replies with a time-stamped information
So, the calculation has to take into account the distance traveled by the train
during the delay between both the last odometry information time stamp and the
Calculation time stamp itself
Odo cycle #100ms
Odometry
calcultation
answer
request
d-FrontEnd
calculation
delay
delay
OBU cycle
beginning
OBU cycle # 300 ms
Estimated d-frontend = estimated n odometry distance – LRBG odometry distance
        + d-ant + (delay x current train speed)
NB : at 350 km/h, the distance traveled by the train during a time cycle (300ms) is about 30m.
So the corrective values are not insignificant￹

---
CONFIDENCE INTERVAL (1/1)
As the train passes over a new LRBG, the confidence interval can be reset,
because the localisation of each LRBG is known with accuracy
0
LRBG 1
LRBG 2
So, as the LRBG changes, the OBU shall inform the odometry and this one shall
reset the confidence interval
But this reset can not be 0 because there always remain some uncertainties:
- uncertainty of physical balise position
- uncertainty of antenna measurement
- (delay between antenna detection and consideration by OBU) x train speed
The sum of these uncertainties shall be < +/- x m. x is given by Q_LOCACC
or a national value
0
LRBG 1
LRBG 2
+/- x m
+/- x m

---
CONFIDENCE INTERVAL (2/2)
Last correction :
The delay between the LRBG pass over and the reset of the odometry values
by OBU shall be taken into account
LRBG 1
0
LRBG 2
+/- x m
Confidence
interval
delay
d-FrontEnd
Max
Estimated
Min
Travelled
distance
0

---
BALISE GROUP ORIENTATION
Balise groups are always oriented in the track normal direction
In one track there are both two linked systems: normal and reverse
A BG can be used for normal and reverse linking
Normal
linking
Track orientation
Reverse
linking

---
BALISE GROUP ORIENTATION
Track 1
Track 2
In front of a point, the system needs a switchable balise to give the
appropriate linking, according to the switch point position
N.B. It is also possible to put the two linkings in a non switchable balise:
the train opens an acquisition window for each linking but only one is present
and can be read

---
LINKED BALISE GROUP
Only linked BG are used as LRBG
A linked balise group is announced by the previous linked BG, in a packet 5
The transmitted linked BG table contains information for the next 4 or 5 BG:
- D_LINK: distance between linked BG (balise n°1)
- NID_BG: BG Number
- Q_LINKORIENTATION: BG orientation (seen from the current LRBG)
- Q_LINKREACTION: what shall the train do if it does not find the BG
- Q_LOCACC: accuracy of the balise location
LRBG2
LRBG0
LRBG1
1 2
1 2 3 4
4 3 2 1
D_LINK1
D_LINK2
Normal
Normal
Reverse
Q_LINKORIENTATION

---
REPOSITIONING (1/2)
If the system needs a good location accuracy (to enter a new domain for
example), it is possible to command a repositioning with a « normal » BG
A packet 16 gives the L_SECTION, e.g. the distance between the next linked
BG and the current BG
LRBG
LRBG
L_SECTION
D_LINK
d-FrontEnd
BG
LRBG
0
LRBG
n
D_LINK - L_SECTION
d-ant
BG odometry distance
n odometry distance
d-FrontEnd = n odometry distance – BG odometry distance
        + d-ant + (D_LINK - L_SECTION)

---
REPOSITIONING (2/2)
Accuracy value can be reset at repositioning place in the same way
a LRBG place
LRBG 1
0
BG
+/- 1m
delay