The data flows and data structures used in the application are the interface between the functional blocks. A clear definition of the data will allow sharing the workload between different groups without causing too much communication overhead.

Data cab be distinguished in data storage which is remembered as a system state: “data stored on-board”, and data temporarily stored.

Data structures shall be designed for:

Inputs (to be synchronised with the API specification):
- structures for messages
- data from other inputs: odometer, DMI, TIU, STM's
Outputs (to be synchronised with the API specification):
- structures for output messages
- data to other outputs: DMI, TIU/BIU, STM's, JRU (not including technical communication, like distributing the system time)
“data stored on-board”

Data structures to store received messages
Messages are received either by radio or BTM (loops are not yet taken into account). The radio will provide a message in one block of data, from a BTM Telegrams (the part of a message sent by one balise) are received, which have to be put together into a message.

Messages contain a header to give the following information:
- valid version
- identifier for the message or BG
- reference to which information is given (identifier of the LRBG), in case of a radio message.
- In case of radio: ack indication
- In case of BG message: information for constructing the message out of the Telegrams and for checking message consistency (balise numbering, message counter etc.)
The message header is used to check the consistency, define the reference for location based data and construct the message out of Telegrams.

Further messages contain “packets” as defined in ss026 chapter 7 (and chapter 6 for baseline 2).

Radio-messages are received as a bit stream in a minimised data format. To allow efficient processing the data has to be stored using standard data-types (fixed point) in structures for individual packets. The chain of components between receiving the message from the antenna to storing packets using standard types is:
radio - EVC basic software – bit walker – filtering.
Functions are assigned as follows to the different modules and functional blocks:
- CRC checking shall be done in the radio. The result of the CRC check shall be made available for the application software (because a CRC error is to handled by the application as a consistency error, i.e. “linking reaction”).
- Translating the bit stream into variables of a standard (fixed point) data-type and store the data in a memory accessible by the application software. The way the data has to be stored depends on the version of the track-side ETCS installation.
  “Pointers” shall be set to packets contained in the message, i.e. an array containing the indexes of the first packet of a certain type. The array shall have one element per possible packet. Each packet shall have an extra field to refer to the next packet of the same type in the message (only possible for a few packet types).
  This shall be done by the “bit walker”.
- Detect the version of the track-side ETCS system, to be done in the application.
- Check on illegal values in the packets. (if detected, set a flag for “consistency error”).
- Couple the location reference to the different packets (those can be different for different packets in case infill information is included in the message, i.e. all packets after packet 136 contain infill information (have to be reference to the LRBG using linking information).
- Translate the identity of the location reference (a BG) from NID_BG to the index and array where the concerning information is stored.
- Check if the packets have to be taken into account or have to be stored in a transition buffer according to the current mode and level (filtering) and mark the packets if they shall be used.

To facilitate the above described functions, a data structure is necessary capable of storing at least 2 complete messages plus extra variables to store the result of CRC checking and the check on illegal values. Further for each packet variables are needed to store the reference position for the information in the packet (NID_BG and index plus array where the BG information is stored). In addition an array is needed to store “pointers” to the start of each packet in the message.

figure xxx
Data structure to store not yet elaborated messages. A special value for the pointer is defined for the case no radio messages are available.
Further pointers to the individual packets are required for efficient elaboration later on.

The different functions can work on the same data structure, i.e. the structure is filled once and is than used up to the point where the packets are elaborated.

BTM-messages are received as a bit stream in a minimised data format per balise (Telegram). To allow efficient processing the data has to be stored using standard data-types (fixed point) in structures for individual packets. The chain of components between receiving the message from the antenna to storing packets using standard types is:
BTM - EVC basic software – bit walker – filtering.
Functions are assigned as follows to the different modules and functional blocks:
- CRC checking shall be done in the BTM per Telegram. The result of the CRC check shall be made available for the application software (because a CRC error is to handled by the application as a consistency error, i.e. “linking reaction”).
- Translating the bit stream into variables of a standard (fixed point) data-type and store the data in a memory accessible by the application software .
  If there is already a Telegram from the same balise stored, then the new data shall overwrite that Telegram. The way the data has to be stored depends on the version of the track-side ETCS installation.
  “Pointers” shall be set to packets contained in the message, i.e. an array containing the indexes of the first packet of a certain type. The array shall have one element per possible packet. Each packet shall have an extra field to refer to the next packet of the same type in the message (only possible for a few packet types).
  This shall be done by the “bit walker”.
- Detect the version of the track-side ETCS system, to be done in the application.
- Check on illegal values in the packets. (if detected, set a flag for “consistency error”).
- Couple the location reference to the different packets (those can be different for different packets in case infill information is included in the message, i.e. all packets after packet 136 contain infill information.
- Compose a message out of the Telegrams if a balise of another BG is found, if all balises of a BG are found, if the maximum distance (12m) since the last detected balise has been passed.
- Gather the BG information needed to build the “reference (coordinate) system”.
- Translate the identity of the location reference (a BG) from NID_BG to the index and array where the concerning information is stored.
- Check if the packets have to be taken into account or have to be stored in a transition buffer according to the current mode and level (filtering) and mark the packets if they shall be used.

To facilitate the above described functions, a data structure is necessary capable of storing at least 15 Telegrams plus extra variables to store the result of CRC checking and the check on illegal values. Indexes (“pointers”) indicating where the information of a completed message can be found shall be set. BG information (location, the identity of the BG, etc.) has to be stored in a separate structure for further evaluation. Further for each packet variables are needed to store the reference position for the information in the packet (NID_BG and index plus array where the BG information is stored). In addition an array is needed to store “pointers” to the start of each packet in the message.

Figure xxx
“Telegram structure”: Structure in which Telegrams shall be stored by the “bit walker”.
A completed message can during the consistency check and the check on linking, be kept in the same structure.

In the example shown on the left:
- A message is just made available consisting of 5 telegrams stored at position 16, 1,..,4.
  If no message is available the pointers “last Telegram of “delivered BG message” and “First Telegram of delivered message have a special value.
  After elaboration of the message and retrieving the packets (done in the same cycle) the pointers will be reset to this special value
- Since receiving the last Telegram of the delivered message, 3 more (5, 6, 7) Telegrams were detected.

“Pointers”:
- “Oldest received Telegram”: the oldest Telegram stored by the “bit walker” which has not been used in a completed message. If no Telegram is waiting for the completion of a BG-message the “pointer” shall have a special value.
- “Last received Telegram”: the last Telegram stored by the “bit walker”. If no Telegram is waiting for the completion of a BG-message the “pointer” shall have a special value.

Transition table
For packages which are not yet to be taken into account a data structure has to be designed to store the packages for later use. The stored packages shall be elaborated if the mode and level for which they are stored is reached (generic condition or shall those be stored with the packet).
The minimum number of packages which could have to be remembered, i.e. the minimum storage capacity to be reserved, is to be determined.

Data structures to store input data from other sources

Other input data:
- TIU: allowed modes, Isolation, brake status (commanded, pressure, inhibited,...)
- DMI: data-entry, acknowledgements, etc.
- STM's: out of scope for the current project. For demonstration purposes an ATBEG can be controlled with only switch on and off functionality.

TIU
The data coming from the TIU is completely specified in ss034. A data structure for storing all possible information shall be designed.

DMI
The data coming from the DMI, consists of inputs required based on information sent to the DMI in the context of a procedure.

An overview of the input and output data is given in annex xxxxx.

Data structures for “data stored on-board”:
1. Location based data (a.o. announced BG's, SSP, speed restrictions, location based level transitions, DMI,..)
2. Actual MRSP and list of targets as a distance from the trains front end. (taking into account the train length for speed increases if necessary).
3. Train Position
4. Reference (Coordinate) system
5. -
6. Direct and conditional orders
7. Intermediate analysis results (linking error, nb of missed BG's, intervention curve passed,......)
8. BG lists for shunting and staff responsible
9. Train data; train running number (including indication valid/not valid)
10. Data describing national rules (national and default values)
11. track data: version, level priority, balise cover marker(s), current RBC ID, current RBC phone number, actual and available radio network ID's
12. Driver data
13. Procedure status information (technical procedures and driver interactions)
14. Parameters tuning procedures (MA request parameters, Train position report parameters,....)
15. System mode and level
16. System status
17. Filtering information (virtual balise cover, reject revocable TRS's,...)
18. Error messages plus status (e.g. reported or not reported)

Below the types of data listed above are further described.

“1”	Location based data
In general “Location based data” is data giving a specific type of information related to a location on the track. Requirements concerning storing:
- The reserved space shall be sufficient to store the maximum number of elements.
- The elements shall be stored in the order they are passed on the track.
- The location shall be available as a distance from the LRBG.
The minimum number of elements for which space shall be available is given in chapter xx, “Management of location based data”. For all types of location based data the same basis structure can be used, except for the location based information which can only contain one element (level transition, reversing area, change power supply, platform conditions, current limitation). The structure is described in chapter xx, “Management of location based data”:

figure xx
Circular data structure for “location based data” (left), plus the structure for one element (above).

“2”	Actual MRSP and list of targets
As described in chapter xxx the MRSP and list of most restrictive targets is not stored as location based data, but as a set of distances with related speed level from the train front end.
At the right the structure of one element of the MRSP or list of targets is shown graphically.

The elements shall be stored in the order in which they are passed. At each cycle the structure shall be update according to the distance driven. As for speed increases the maximum distance and for speed decreases the minimum distance is valid, the order of the elements in the MRSP may change during driving from the LRBG.

“3”	Train Position
The train position shall be available for the trains front end, the rear end and the active antenna as a minimum, estimated and maximum distance from the nominal position of the LRBG:
	Minimum	Estimated	Maximum
front	X	X	X
rear	X	X	X
antenna	X	X	X

To be able to retrieve this data the following data is stored:
- The measured distance (raw data from the odometer) stored as a passing location (of the active antenna) for the LRBG
  (to be stored in the structure of the “list of passed BG's”).
- The passing direction of the LRBG (nominal or reverse): for reporting to the RBG.
  (to be stored in the structure of the “list of passed BG's”).
- The antenna (A or B side) which read the LRBG
  (to be stored in the structure of the “list of passed BG's”)
- The distance between the antenna A and cab A
- The inaccuracy in the distance between the antenna A and cab A (installation inaccuracy only)
- The distance between the antenna A and cab B (installation inaccuracy only)
- The inaccuracy in the distance between the antenna A and cab B
- The distance between the antenna B and cab A
- The inaccuracy in the distance between the antenna B and cab A (installation inaccuracy only)
- The distance between the antenna B and cab B (installation inaccuracy only)
- The inaccuracy in the distance between the antenna B and cab B

Together with the inputs “actual train position” and the “train orientation”, all combinations given in the table above can be generated.

“4”	Reference (Coordinate) system
The data stored shall allow to calculate the distance between the train and a track-side element whose location is given as a distance from the nominal position of any BG. Therefore data shall be available concerning the relation between the distance from the nominal position of the LRBG and the distance from the nominal position of any other BG (further called ORBG), see figure xxx. This distance is further called the “correction distance” and is BG specific. Therefore is shall be stored in the data structure for detected and announced BG's.
This “correction distance” can be derived from linking (exact) or from odometer data (with a tolerance). Further the possible distance between the position where a BG is detected and it's nominal position is to be taken into account.

Figure xx
Calculation of the distance from the train to an a track-side element (“Location”)

Therefore for each BG already passed, in reference to which the location of any track-side element is given a minimum and maximum correction distance shall be stored in order to be able to calculate the minimum and maximum distance between the train front end en the track-side element:

Distance between train and location =
Distance from ORBG – Train Position (I.r.t. LRBG) - the stored correction distance (all including tolerances).

As the Location of a track-side element can also be given in reference to a BG in advance of the train (infill information), the same correction distance shall be available for announced BG's. This is only with one difference. For announced BG the exact linking distance is available (if not the infill information can and must not be taken into account). The correction distance exact (no minimum and maximum), and equal to the linking distance.

This leads to the need for two data structures, one storing the correction distances for already passed BG's, and one storing the announced (linking) distance from the nominal position of the LRBG to the announced BG's. The latter structure also contains the data needed for checking the linking consistency, i.e. the expectation window. A graphical representation of the data structure is given below:

figure xxx
Data structures for announced, detected linked and detected unlinked BG's.
- LRBG: “last relevant BG” = the last detected linked BG
- Last detected BG: can be different from the LRBG if the last detected BG is marked as “unlinked”
- Most rear actual BG: most rear BG to which one or more “Locations” refer as being their ORBG ( original reference BG). All BG's more in rear may be deleted from the list.
- Most rear BG: the most rear BG whose information is still stored in the “list of detected BG's”
- “Oldest BG”: BG to which all “Locations” with an ORBG in rear of the “most rear BG” refer. This is used if the “List of detected BG's” is full. Between the “oldest BG” and the “most rear BG” no linking distance is available. Therefore the accuracy for the concerned locations will decrease.
- linking hole: Number of linked BG's for which no linking information is available (see figure xx).
- skipped BG: Linked BG which was detected when no BG's were announced, but which is not included in linking information received after wards (see figure xx)
- “pointer”: index of the element in the data structure where is referred to.

“6”	Direct orders
Direct orders can be given for several actions, e.g. command the service or emergency brake, “stop if in staff responsible” etc. Direct orders which have immediate effect at the first evaluation like direct level and mode transitions (have immediate effect in the functional block “filtering” because they shall be taken into account at filtering further information in the message) are not stored.
Direct orders shall be stored in the internal data structure to allow the correct execution of the order by the concerning functional block. For each possible order a field shall be reserved, i.e. an array with a field for every possible order shall be build.

This data structure is needed to avoid getting event driven software, as the orders are stored and read by the a functional block which is commanded cyclicly.
Direct orders to be stored (as a flag or variable):
- command service brake.
- “stop in staf responsible”
- SR authorisation
- Exit of trip mode
- Inhibition of revoking TRS's

{ To what extent shall mode changes following from input data be taken into account before filtering?}

Intermediate analysis results (linking error, nb of missed BG's, intervention curve passed,......)
Just like direct orders, some analysis results shall lead to a certain specified action. For example, having a consistency error shall lead to the linking reaction (given from track-side or the default value which is command service brake). Just like direct orders those intermediate results are stored as an order for other functional blocks, in stead of immediately (event driven) calling the specific function.
Intermediate results to be stored (as a flag or variable):
- From BCM: EB intervention, SB intervention, acoustical warning, Vsoll, Vwarning,...
- From linking consistency checking: type of linking reaction, number of missed BG's
- From message consistency checking: type of linking reaction
- …...

“7”	Intermediate results

source	sink	Description	Relevant requirements
		“The onboard reacts according to a linking reaction set to “trip”, “the train/engine receives and uses a trip order given by balise”, “unconditional emergency stop message is accepted”	§4.6, condition [17, 18, 20, 32]
		“a National Trip Procedure is active”	§4.6, condition [35, 38]
		“override” function is active” TODO maybe internal data	§4.6, condition [42, 46]
		“The system version number X of a received balise telegram is greater than the highest version number X supported by the on-board equipment”	§4.6, condition [65]
		“A balise group contained in the linking information is passed in the unexpected direction”	§4.6, condition [66]

“8”	BG lists for shunting and staff responsible
Together with the order to go to shunting or to staff responsible a list of BG's which may be passed can be given. As the system can only be in one mode at a time, one data structure to store the BG's is sufficient.
The data structure shall consist of an array storing the identities of the BG's which may be passed. As the passing order is not always predictable it doesn't make sense to reorder them. BG's may thus be stored in the same order as they were received.
The information cannot be updated as it is only sent with the transition order.

“9”	Data describing the train
To allow the usage of the system on all different train types, data describing the specific train shall be stored. The source of the data can be the TIU, the data entry unit or default values. Data to be stored includes:
- Train category(ies)
- Train length
- Traction / brake parameters
- Maximum train speed
- Loading gauge
- Axle load category
- Traction system(s) accepted by the engine
- Train fitted with airtight system
- List of National Systems available on-board
- Number of axles

“10”	Data describing national ruling
Maximum speeds, braking curve margins, roll away distance, timing for certain conditions, procedual information etc. may differ from country to country.
Therefore a list of national values is defined (ss026, A3.2). These national values shall be stored on board, to be available for all functional blocks.

For those national values, defaults can be defined for the case no national values have been received from track-side. A simular structure shall be provided to remember those default values.

“11”	Track data
The version of the track-side ETCS system and the priority of levels supported from track-side shall be available for the functional blocks. Data structures to store this information in the same format as it is received from track-side shall be provided.

“12”	Driver data
Driver data is used when displaying data to the driver (language) and for juridical recording (driver ID). A data structure shall be defined to store all possibly available driver data.

“13”	Procedure status information
In the SRS (especially ss026 chapter 6) a number of procedures between track-side, train and driver are described, e.g.
- data-entry
- reporting train position
- SoM, EoM
- Train data management....
- text message acknowledgements
- establishing and ending a connection to the RBC
- RBC-RBC hand over
- transition to shunting
- transition to staff responsible
- …...
For each of these procedures the status shall be remembered, in some cases including the time since specific events.
Therefore for each procedure a global data structure shall be designed to remember the status of each procedure. This will be organised per subsystem where a question can be put (DMI and Radio).

DMI RELATED DATA STRUCTURES
Concerning procedures the following types of data have to stored/buffered for the interaction with the driver:
- “Driver requests”:requests to the driver to acknowledge, validate or enter data.
- “Fixed text messages”: information to be given to the driver. The texts can be fixed because the procedures are all exactly defined, all text can be determined before.

Driver requests
Several procedures or requests from track side can lead to a request to be sent to the driver. The generated requests shall be buffered in an internal structure. The DMI management function can than check if a request is stored in a predefined priority; except for data entry, which is handled in a different structure, only one request shall be “pending” (waiting for driver response) at a time.
{The API allows to sent more requests and let the DMI buffer those, sending only one is however not in conflict with the API}
A request can have the status “set” (a request shall be sent to the driver), “pending” (question sent to the driver, no answer yet), “available”, (result available, but not yet elaborated), “not answered” (driver didn't respond, negative result not yet elaborated), or “not set/elaborated” (= initial state: no request set, pending, available or not answered).
For a pending request a timer shall be set. For each type of request a time-out value can be stored (i.e. the data structure is available)
A request can be withdrawn if the timer expires or if a request with a higher priority has to be sent. In the latter case the withdrawn request shall be stored as “set” again.
The results shall be stored in the “internal data structure” (“data stored on-board”), or in some cases (indicated in the table below) in the data structure for the requests.

Array with possible requests to the driver:
Name	Description	source	Data structure for result
	Request to enter/validata driver ID (depending on the status valid/not valid)	Procedure SoM, 5.4.3.2 S1	“12”, driver-id + state (valid/not valid)
	Request to the driver to enter/validate the level (depending on the status valid/not valid)	Procedure SoM, 5.4.3.2 S2	“15”, level + state (valid/not valid)
	Request to the driver if he wants to enter a new network ID (Y/N)	Procedure SoM, 5.4.3.2 S3	Result to be stored in the list of requests.
	Request to the driver to choose between: use the last phone number RBC-ID/phone number, use EIRENE short number, enter or validate RBC-ID/phone number	Procedure SoM, 5.4.3.2 S3	“11”, RBC-ID/phone number + state (valid/not valid)
	Request to the driver to choose between: “shunting”, “non-leading”, “data-entry”	Procedure SoM, 5.4.3.2 S10	{ result to be stored in the driver request buffer }
	Request to the driver to enter/validate the train running number (depending on the status valid/not valid)	Procedure SoM / 5.4.3.2, S13	“9” train running number + state (valid/not valid)
	Request to the driver to select “start”	Procedure SoM / 5.4.3.2, S20	Result to be stored in the list of requests.
	Request to the driver to acknowledge the selected national system	Procedure SoM / 5.4.3.2, S22	Result to be stored in the list of requests.
	Request to the driver to acknowledge unfitted mode	Procedure SoM / 5.4.3.2, S23	Result to be stored in the list of requests.
	Request to the driver to acknowledge SR mode	Procedure SoM / 5.4.3.2, S24	Result to be stored in the list of requests.
	Request to the driver to acknowledge OS mode	Procedure SoM / 5.4.3.2, S25	Result to be stored in the list of requests.
	Request to the driver to acknowledge LS mode	Procedure SoM / 5.4.3.2, S25	Result to be stored in the list of requests.
	Request to the driver to acknowledge SH mode	Procedure SoM / 5.4.3.2, S25	Result to be stored in the list of requests.

Fixed text messages
xxx

Array with possible fixed text messaged to the driver:
Name	Description	source	Data structure for result
	“Radio connection failed”	Procedure SoM 5.4.3.2, A29
	“Radio session set up failed”	Procedure SoM 5.4.3.2, A32
	“Train rejected by the RBC”	Procedure SoM 5.4.3.2, A40

RBC COMMUNICATION RELATED DATA STRUCTURES
xxxxxx

“14”	Parameters for procedures
As the requirements concerning procedures may differ, parameters are defined to tune the procedures. (timing requirements, etc.). Data structures to store this information in the same format as it is received from track-side shall be provided.

“15”	System mode and level
The system mode and level shall be available to all functional blocks at any time. Therefore variables to store the current state and level shall be defined.

“16”	System status
Data structures are necessary to store the current status of the subsystems (Radio, BTM, LTM, STM, JRU, odometer, TIU, brakes).

“17”	Filtering information (virtual balise cover, reject revocable TRS's,...)

“18”	Error messages plus status (e.g. reported or not reported)

Data structures to store messages to be sent to the RBC
The information needed which as to be sent to the RBC is provided by “train supervision”, “mode/level management”, diverse procedures etc.
To sent them to the RBC the information has to be build in a specific format (specified in ss026, chapter 7 and 8). This structure has to be synchronised with the API specification

Data structures to sent to subsystems (DMI, TIU/BIU, JRU, STM)
Information to be sent to the DMI and TIU/BIU shall be build in data structures as described in the API specification.
The JRU and STM are out of scope for the current itteration.