It is discussed what shall be done first: checking linking consistency (on the BG information) or checking message consistency (on the data in the message).

Check linking consistency, i.e. checking if a BG is found inside the expectation window, and if the BG's are found in the right order.
Questions:
- if linking consistency is OK, i.e. balise 1 is found within it's expectation window, but the message is not consistent, may the BG be used as an LRBG in that case?
- What shall be deleted in case of a linking error: only the BG data or also the message?
  If the BG information is deleted but not the message, then location based data can come available without a reference. Or shall a BG outside it's expectation window be stored as if it was an unlinked BG?

Check message consistency, i.e. check if the message is complete and received correctly (no CRC errors). If errors are found however, a difference is made between BG's found while BG's were announced and BG's found while no BG's were announced. This seems strange but is in fact not more than a default value;
the linking reaction is only known from the linking information (packet 5), if this information is not available for the detected BG a default shall be used, so linked BG's which are found inside the expectation window are treated the same as linked BG's when no linking info is available, but for the latter a default reaction is used.
Inconsistencies?:
- What shall be done with information from the expected BG, found outside the expectation window? In 3.16.2.3.1.1 it is only stated that the BG shall not be used as LRBG (thus can be treated as unlinked) however in 3.16.2.4 the situation is not mentioned anymore.
- The on-board shall expect the BG's one by one. So what if a BG is included in the linking information, but is not the expected? Acc. To 3.16.2.4.3 such a message is not rejected?
- What's the difference between “shall not be taken into account” (par 3.4) and “message is rejected” (par 3.16.2.4), and “ignore a BG” (par 3.16.2.3)?

Considerations:
- If a BG is not found at it's expected location, how is than guaranteed that the location based data given by the BG is correct?
- If a BG message is corrupt, how can in that case be guaranteed that the BG identifier is read correctly?

Conclusion:
If a BG is found at an unexpected location of the data is corrupted the location of the BG and the message given by the BG will both be deleted.
The order in which the functions are executed is arbitrary.
Functional and data architecture ETCS on-board

Jan Welvaarts
# Version management
Number	Date	remark	responsible
0.1	10-10-2014	First version	JW

# Content
# Preface
This document defines the rough structure of the ETCS functions and internal data structure (IDS). Purposes:
- Structure the data to keep it manageable in the functions.
- Create a common understanding of the structure (not yet using software tooling)
- Synchronize the structure for variables defined for different functions (by different groups), i.e. define the interfaces between functions.

The application (excluding STM management) shall result in speed monitoring (service and/or emergency brake interventions) and a presentation on the DMI of speed + braking curve, the speed profile ahead and further texts and icons. Those shall be based on inputs coming from track-side (BG's and radio), from train borne (train parameters), from the driver and the odometer. A stepwise elaboration from the input information to the required outputs is shown below:

To be included

figure xx
Rough functional and data structure

Further in this document data structures and functions will be further elaborated.

# Overall data structure

Many variables contain different information, but shall be structured in the same way. The most obvious example is location based information. Locations are necessary for many data structures and shall therefore be stored in the same way. This is not guaranteed if different are defining variables independent from each other. Therefore This document will define a top level structure for the date dictionary and set requirements for more detailed variables. The structure of the internal data will be targeting the use of the data (i.e. it will not be a copy of the source).

Roughly three types of internal data are distinguished:
- Location based information describing the infrastructure.
- Description of the train (including train position).
- Status information: mode, level, dmi status etc.

The “variable categories” shown in figure 1. Variable types to be used to describe the information listed shall be decomposed down to the level of standard data types (boolean, word, integer, double,....).

The first chapter defines a number of requirements the internal data structure has to fulfill (i.e. the requirements).

The second chapter describes for each of the “variable category” which information it globally contains, where the information is coming from and what the use of the information is.

In the third chapter the individual data structures is described, starting with the “coordinate system” as the “list of passed BG's” serves as a basis for all location based information.

In the last part the internal data structure will be detailed using variables defined by the groups which are defining functions.

Figure xxx:
High level data structure for the internal data
stored in the internal data structure (IDS)

	?	G / positioning	H / Filtering	A / Configuration, RBC connection	B / Route data	C / DMI / Text messages	D, / Location dependent / Mode/level	E / Mode/Level	F / STM
Messages / RBC->train	24	45		8, 39, 40, 41	2, 3, 9, 33, 37	34	43	6, 15, 16, 18, 27, 28, 40, 32, 38
Packets / Track->train		5, 136, 16	0, 6, 64, 134, 145, 254, 255	3, 42, 45, 57, 58 (loc dep.), 131 (loc dep), 140, 141, 143,	12, 15, 21, 27, 39, 40, 51, 52, 65, 66, 67, 68, 69, 70, 71, 88, 133, 138, 139, 80,	72, 76, 79	13, 41*, 46, 137	2, 49,63, 90, 132, 135, 41*	44

* special value for immediate level transition

Above: table with messages sorted to type of information

# Principles
In this chapter a number of principles will be set to tune the format of the variables proposed by different groups which are defining functions:

Principle	explanation	ID
The internal data structure shall be targeted on the user of the data not primarily on the source.	The input part of the system shall translate the different formats of information to one standard to simplify the actual functionality of the system.
The data structure shall minimize the reanalysis of data if other data is received. I.e. not shift data, avoid changing data for all stored locations if a new LRBG is detected, etc.	By avoiding peaks in the processor load when BG's are detected and/or messages are received, the system will become more predictable.
All data in the data structure shall be accessible without searching, i.e. pointer structure shall make searching superfluous.	As all necessary entries are known, this can be realized and will safe (unpredictable) processor time.
All data types shall be based on a limited number of standard data types. (for now): Boolean, word, integer, double, text	Eases the validation
No redundant data shall be stored.	Storing the same information more than once can lead to mistakes, requires more memory and more attention when updating data. / E.g. the accuracy of locations depends only on the BG which has sent the information plus linking and odometer information. The accuracy shall therefore be stored in the structure describing the BG.
Similar data shall be stored in similar structures.	e.g. a lot of data is location based. This shall not be stored partially incremental and partially from one reference. / All distances in the same, all locations..., all times..., all speeds,.. etc.
Memory is not dynamically allocated. For each type the maximum number of instances shall be determined. This number can be created at start-up	Dynamic allocation of memory increases the number of states and therefore the validation effort.

# Data structure and functions for distance calculation

As further detailed in chapter 4, a lot of information given from track side to the on-board is valid for certain locations (is “Location based”). These “Locations” are given from track side in reference to a BG specific for a group of “Locations” given in the same message. The ETCS on-board shall continuously calculate the distance from the train to all “Locations”.

The distance between the train and a “Location” can be calculated using one reference point in rear of the train for the train and all “Locations”. By subtracting the distance driven from this reference point, from the distance between the reference point and the “Location”, the distance between the train and the “Location” is found. Before this is possible, the distance (including tolerances) between the reference point and all “Locations” shall be calculated. As the delta compared to the original reference (given from track-side) is equal for all “Locations” given from track-side with the same reference BG, this calculation is only necessary once per BG.

The choice of the reference point is arbitrary. The only real choice is taking a track side location or the train as a reference. As the latter would lead to continuously updating all track-side “Locations”, it is more efficient to choose a track-side reference point.
Because the Train Position has to be calculated in reference to the on-board LRBG anyway according to the SRS, it was decided to use the nominal position of the on-board LRBG (last relevant balise group, used as reference in the communication with the RBC) as the reference point for distance calculations[1].
[1] The discussed alternative was always taking the last passed BG, also if this is an unlinked BG. This was however rejected by the majority of the team (workshop Berlin, november 2013).
For simplicity, the antenna position of the train will be used in the calculations. The distance will be corrected for the front end of the train after wards.

If a “Location” was given from track-side as a distance from the on-board LRBG, no calculations are necessary. If a “Location” is given by the track side as a distance from the nominal position of another balise group (BG) in rear of the LRBG then the distance between the LRBG and the “Location” shall be calculated. The BG from which the distance to a “Location” was given by track-side will further be called the “original reference balise group” (ORBG) for the specific “Location”.

To calculate the distance between the nominal position of the LRBG and the “Location” including tolerances, a “correction distance” (D_correction including it's tolerances) is defined. This “D_correction” is specific for every BG in rear of the LRBG.
Figure xx
Calculation of the distance from the train to a “Location”

So for every BG in rear of the LRBG which is used as an ORBG for a “Location” which is not yet passed, the correction distance “D_correction” shall be known including tolerances.

This calculation is done for “linked” BG's by starting from the LRBG and stepping backwards through the list of BG's, adding the additional “Dcorrection” for every BG further in rear. In an iterative process. After this first step the correction distance for unlinked BG's is calculated based on the correction distance of the first linked BG in rear or in advance of the unlinked BG.
Formulas for the calculation of the additional correction distances including tolerances are given in “Train Position and Locations v0.16” chapter 4.
Formulas for the calculation of the “Train Position” in reference to the nominal position of a new LRBG at the moment the new LRBG is detected (the antenna position including tolerances) are given in “Train Position and Locations v0.16” chapter 3.

Below data structures will be defined for the “Train Position” and a “Location”. As described above each “Location” is given in reference to an ORBG. To remember the essential data for those ORBG's a data structure will be defined for a list of BG's.

## Data structure for the “Train position”
The train position shall be defined as a distance from the nominal position of the on-board LRBG. At “Train position” is calculated initially for the moment the new on-board LRBG is detected. The odometer data valid for the moment the LRBG is detected, is stored in the BG data structure. Using this data in combination with the initial “Train Position” in reference to the nominal position of the LRBG, the actual distance from the train front end to the nominal position of the LRBG (including tolerances) can be calculated at every point in time. This calculation is done (using inter and extrapolating of odometer data) for the starting time of each calculation cycle.
Figure xx
Data structure for the “Train Position”
The variables which have to be calculated from the stored data are:
- The actual nominal front end distance from the nominal position of the LRBG (integer)
- The actual minimum safe front end distance from the nominal position of the LRBG (integer)
- The actual maximum safe front end distance from the nominal position of the LRBG (integer)
- The nominal rear end distance from the nominal position of the LRBG (integer)
- The minimum safe rear end distance from the nominal position of the LRBG (integer)
- The maximum safe rear end distance from the nominal position of the LRBG (integer)

## Data structure for a “Location”
A “Location” is given from track-side as a distance from the nominal position of a BG (“ORBG” for the specific “Location”). The information will be stored in the received format, i.e. index of the element in the list of BG's where the information on the ORBG is stored, and the distance from the nominal location of this ORBG to the “Location”.

If a “Location” is used the distance from the nominal position of the LRBG shall be known (including eventual tolerances). The “D_correction” needed to calculate the distance between the “Location” and the nominal position of the LRBG from the distance between the “Location” and the nominal position of the ORBG shall be stored in the data structure for the ORBG. Therefore the index of the element in the list of BG's where the ORBG can be found, shall be stored in the data structure for a “Location”. At every detection of a new LRBG, the minimum, estimated and maximum distance between the nominal position of the LRBG and the “Location” are calculated and stored.

The distance from the nominal position of the ORBG to the “Location” is stored as a positive value in the direction in which the train is oriented.

Figure xx
Data structure for a “Location”: the reference to the ORBG is an index of the element in the data structure (array) in which the BG's are stored (List of BG's).

At the data structure for a “Location” two indexes are stored. One is an index continuously summing up if a BG is detected, i.e. the first detected BG after start-up will have index “1”, summing up till the system is reset again (e.g. deleting all location based data). The second index is an index which refers to the circular buffer where the “list of detected BG's” is stored, this one starts at 1 at every new cycle:
Index_2 = Index_1 – N*truncate(index_1/N) where N is the size of the “list of detected BG's”.
Index_1 is further called Index_total
Index_2 is further called Index_LoDBG (List of Detected BG's)

“Index_total” is used to check if a “Location” refers to a BG which has already been deleted from the “list of detected BG's”. If so the reference shall be changed from the ORBG to a worst case reference. If a BG is detected while the “list of detected BG's” is full, the oldest BG will be deleted from the list and all BG's referring to this BG as an ORBG will further refer to a field where the oldest known BG is stored. This implies also recalculation of the nominal distance between ORBG and the “Location”. If a BG is deleted from the “list of detected BG's” while the list is not full, then the data concerning the new rearmost BG in the list will be copied to the field where the oldest known BG is stored. As no linking data is stored in rear of the rearmost BG in the “list of detected BG's”, the distance between the “oldest known BG” and the rearmost BG in the “list of detected BG's” can only be based on odometer data, leading to increased inaccuracy.
This function will be described in detail in “deleting passed locations”, and “update the list of detected BG's”.

## BG's as a reference for the Train Position and Locations
BG's will be stored in indexed array's in a way that they do not have to be shifted from one element to another. Actions which are foreseen are:
- Storing announced BG's, i.e. receiving, storing and replacing new linking information.
- Detecting a linked BG (new LRBG), calculate D_correction for the whole chain of linked BG's and for the stored unlinked BG's
- Detecting an unlinked BG
- Storing linking information for already detected BG's (rare situation). This is possible as requirement 3.6.4.7.2 “new linking information (packet 5) is replacing all linking info from the LRBG” is interpreted as all linking information from the LRBG used as reference by the RBC. That LRBG can be up to 8 BG's in rear of the on-board LRBG.

Considerations:
- If announced BG's are stored in the same structure as the detected linked BG's, the already available information doesn't have to be copied. But if announced BG's are stored in the same structure as detected linked BG's, then unlinked BG's cannot be stored in this structure without shifting information in case an unlinked BG is detected while linked BG's are announced.
- Skipped BG's and unlinked BG's can be handled in the same manner; if a list of BG is evaluated, the index of the last BG for which was linking information is known as well as the index of the BG it was referring to. Therefore for BG's stored in the same structure as the linked BG's, the information is available to calculate D_correction from information available for the previous and next linked BG.
- A further special situation is the combination of a regular case where linked BG's are only included in linking information for one direction, with the rare case of receiving linking data for distances in rear of the on-board LRBG. Therefore it is not guaranteed that the linking chain can be built by simply stepping through all elements.
- Linked BG's are also used in communication to the RBC. A minimum of 8 shall be remembered. This is more complicated if unlinked BG's are stored in the same structure.
- An announced BG could be missed, in that case linking distances have to be updated. In case announced and linked BG's are stored in the same structure this would lead to shifting information.
- Linked BG's have to be deleted from the structure in the same order as in which they were received.
- Unlinked BG's will be deleted in a random order (when the related “Locations” are all passed), this will lead to a random filled data structure with a need to manage the available “empty fields”.
Concluding, there are three options:
- storing announced BG and detected linked BG in the same structure
- storing linked and unlinked BG's in the same structure
- storing linked, unlinked and announced BG's all in their own structure.
Based on the considerations above storing in two structures, one for announced and one for detected BG's, has a slight preference:

figure xxx
Data structures for announced, linked and unlinked BG's.
- LRBG: “last relevant BG” = the last detected linked BG
- Last detected BG: can be different from the LRBG if the last detected BG is marked as “unlinked”
- Most rear actual BG: most rear BG to which one or more “Locations” refer as being their ORBG ( original reference BG). All BG's more in rear may be deleted from the list.
- Most rear BG: the most rear BG whose information is still stored in the “list of detected BG's”
- “Oldest BG”: BG to which all “Locations” with an ORBG in rear of the “most rear BG” refer. This is used if the “List of detected BG's” is full. Between the “oldest BG” and the “most rear BG” no linking distance is available. Therefore the accuracy for the concerned locations will decrease.
- linking hole: Number of linked BG's for which no linking information is available (see figure xx).
- skipped BG: Linked BG which was detected when no BG's were announced, but which is not included in linking information received after wards (see figure xx)
- “pointer”: index of the element in the data structure where is referred to.

figure xx
Difference between missing linking information and a “skipped” BG, i.e. a BG which is marked as linked but is not included in linking information received after it was detected.

There are several reasons to remember original BG information:
- According to the ERA SRS it is required to remember the last 8 linked BG's which are detected, because the RBC can use those as a position reference for information sent to the train.
- In the case the linking information between this BG and the current LRBG is not (completely) known, the accuracy with which “locations” are known depends on the BG from which they were sent.
  This is the case for unlinked BG's, and linked and already detected BG's for which the linking distances are not (yet) available.
- The accuracy with which “locations” are known, is equal for all locations with the same original reference. References with the same accuracy (BG's between which the linking distance is known) could be grouped. The information about the grouping shall than however be stored with all the locations. This leads to an unnecessary processor load.
- For the data concerning “Locations” referring to linked BG's more than 8 BG's in rear of the LRBG, the reference BG could be changed (especially when linking information is available). This would however lead to extra or different processing for those “Locations”. Therefore it's easier to just remember all linked BG's until all related “Locations” are passed.
- Peak loads shall be avoided. The alternative for storing BG information to calculate the location of “Locations” is storing the information at all “Locations”, which potentially causes higher processor loads. (and for the last 8 linked BG the relation between BG and “Location” has to be remembered anyway for the case linking information is received from an LRBG (used by the RBC) in rear of the on-board LRBG.

## Data structure per BG
After detecting a BG, the information concerning passing direction, expectation window, linking reaction and information if the BG is a repositioning BG, is used to decide if and which information shall be used, and to check the consistency of the BG. After accepting the information, from this data only the passing direction is still needed for position reports to the track-side.
The further information is used to update the “Train Position” and is stored to be able to locate all related “Locations”. The minimum set of data to be stored per passed BG is:
For structuring the list of BG's:
- For linked BG's when linking information is available: The index of (“pointer” to) the previously detected linked BG.
- For linked BG's when linking information is available: The index of (“pointer” to) the next detected linked BG.
  In case of the LRBG this variable contains the index of the “expected BG” in the structure of “announced BG's”
- Correction distances which give the minimum and maximum distance which shall be subtracted from the distance to “Locations” referring to the BG, when the distance between the trains front end and the “Location” is calculated (in that calculation also the “Train Position is subtracted from the distance to the “Location”):
  *	Dmin_correction
  *	Dmax_correction
  The values are calculated according to the formulas given in “calculating location and train position 0.0.16”, and will be recalculated at every detection of a new LRBG.

BG information:
- The BG identifier (NID_BG/NID_C)
- The inaccuracy of the positioning of the BG:
  *	Dmin_nom-det
  *	Dmax_nom-det
  The minimum and maximum distance from the nominal position of the BG to the detected position of the BG (D_nom-det is negative if the detected position is in rear of the nominal position). The values are calculated according to “calculating location and train position 0.0.16” based on the received variable “LOC_ACC”, the detection accuracy for a BG and in some cases the linking distance from the previous LRBG.
- The linking distance (if available) to the next (more in advance) linked BG. (positive in the direction of the train orientation)
  In case of the LRBG this variable is unknown
  If the BG is a repositioning BG this information can not be used, causing a “linking hole”
- The measured absolute position at which the BG was detected: time stamped odometer data.
- The passing direction (can be unknown in case of the BG being a single BG)
- Information if the BG was marked as linked , i.e. can be used in communication to the RBC.
- Distance to the furthest location given by the BG: to determine if all locations given by the BG are passed, thus the BG can be deleted? (unless there are less than 8 linked BG's in memory)

Figure xxxx
Data structure for a detected BG

Per announced, but not yet passed BG the following information shall be stored:
- The BG identifier (NID_BG/NID_C)
- The inaccuracy of the positioning of the BG: LOC_ACC
- The linking distance from the first linked BG in rear (as received using packet 5).
- The announced passing direction
- The linking reaction
- Information if the BG is a “repositioning BG” for which the linking distance is not exact.
A link to the next or previous announced BG is not necessary. As the list is completely filled, the next BG will always be found at the next index. The data structure per BG is shown below:

Figure xx
Data structure for an announced BG

Linking distances for detected BG's are used for calculating the correction distances from BG in rear of the LRBG starting iteratively from the LRBG. The linking distance between two BG's is needed when calculating the correction distance for the rearmost of the two BG's using the correction distance of the most in advance BG of the two, and the linking distance between the two BG's. Therefore the linking distance between two detected linked BG's shall be stored at the data structure for the rearmost of the two BG's
As linking distances for announced BG's are given from the previous linked BG's, the linking distance between two announced BG's shall be stored at the data structure for the furthest (most in advance) BG.
The above is graphically shown in figure xxx.

Figure xxx.
Data structure where the linking distance between two BG's is stored; for detected at the rearmost, and for announced BG's at the furthest (as the information is received from packet 5).

Below it is explained how the data structure supports the functions for managing .

## Functions for managing the BG structures and Train Position when a BG is detected
BG information is stored to use the BG's as location-reference for “location based information” (see chapter 5).
Managing BG structures includes, storing information on announced BG's and updating information concerning announced and already detected BG's when a new BG is detected. Storing received linking information is examined in chapter 5 “Datastructures for and management of specific location based data”. Below the management of BG structures when a BG is detected will be examined.

To be able to use BG's as location reference the position of detected BG's is stored with a time stamp of the moment of detection. Together with the identity of the BG, the linking distance from the (old) LRBG, the passing direction, an indication that the BG is linked, the minimum and maximum distance between the nominal and detected position of the BG and the location of the furthest location referring to the BG, this information is stored as “BG info”:

Figure xxx
BG info as composed by the function “Build BG message”.
This structure contains the “BG information” which is stored per BG in the “list of detected BG's” (see “BG structure”).
The linking and data consistency flags are determined by the functions “BG-msg consistency” and “check linking consistency”:
- value 1: linking inconsistency
- value 2: message inconsistency
- more?

A BG can consist of 1 to 8 balises. Each balise gives one telegram. Independent from the order of reception (1 to n or n to 1), balise 1 is used as the location reference (although there is an exception if balise 1 is missed). A function “build BG message” (function “2”, see figure xxx) is defined to combine the telegrams in one message and to compose the information on the BG (“BG info”). Partly received BG-messages (telegrams and BG information) shall be stored in a dedicated data structure awaiting the completion of the message and “BG info”. The information in this structure can also be used by the function checking linking consistency, to know if the end of the expectation window is reached without finding balise 1.
Location based information received in the packets contained in the message is given in reference to the position of the sending BG (i.e. to the position of balise 1).

Radio messages are assumed to be given complete by the “radio” and the “bitwalker”. In the radio messages an identifier of the BG (NID_BG/NID_C) is included, to which all location based data in the message refers. For on-board usage this identifier shall be translated in the index of the “list of detected BG's” where the BG information can be found. This is realized in the function “link reference BG” (function “8”, see figure xxx). This function applies to radio as well as to BG messages.

Before using the message and BG information the consistency of the message shall be checked, i.e. it is checked if the information is complete and not corrupted (see functions “3” in figure xxx). In case of consistency errors the message shall be deleted and an error action is initiated (indicated with a question mark, as this function is to be defined).

If BG's are announced, i.e. the location where they shall be found is given, then the detection position (of balise 1) shall be checked (see function “4” in figure xxx). However it is not the detection position but the nominal position of a BG which is used as a reference for locations in the ETCS application. Therefore the minimum and maximum distance from the nominal location to the detection location shall be calculated, these values will be used as minimum and maximum Train Position (from the nominal position of the BG) at the moment the BG is detected. This calculation is done in function “5” in figure xxx. After this calculation the BG information (“BG-info”) is complete to be stored in the “list of detected BG's” (see function “6” in figure xxx). Based on the “list of BG's” (whether a new BG was added or not), the Train Position at the start of the cycle can be calculated from the minimum and maximum distance from the nominal position of the LRBG to the detected position of the LRBG, and the minimum and maximum distance run between detecting the BG and the start of the cycle. This calculation is performed in function “7” (see figure xxx).

Before using the information which was contained in packages in the message, the individual packages are “filtered”, i.e. it is checked if the concerning information shall be accepted or rejected under the current mode and level. In case of an upcoming level or mode change a third option is to store the received information in a “transition buffer” for later use. The filtering is done in function “9” (figure xxx). After this step the received packets are selected and stored for further processing in specific data type dependent management functions (e.g. “store linking information”, “manage MA”, “build SSP”, “gather speed restrictions”,.... see chapter 5).

figure xxx
Architecture of managing BG structures and Train Position

The numbering in figure xxx indicates the order in which the functions shall be executed.

Results leading to later actions shall be stored in a specific data structure (“CONDITIONS”). Variables determined by the functions above are:
- “number of missed BG's”
- “linking reaction to be executed “ (1: none, 2: service brake, 3:...)

The data structure “CONDITIONS” shall also be used to store all conditions leading to mode or level changes. The changes shall take effect at the end of the calculation cycle.
Intermezzo on performance requirements:

A decision to be taken is the number of BG's which the system shall be able to handle in one cycle. This number is depending on the length of a cycle and the maximum number of BG's which can be detected in a certain time frame. The following requirements were found:
- According to ss40 4.1.1.6 max 8 balises are received per 800ms
  thus in a 100ms cycle the average over 8 cycles is maximal 8
- Minimum distance (ss36 5.6.3: 10ms between two balises)
- No minimum distance between BG's?
Further time constraints (ss41) allow certain response times for orders given from track-side:
ss41, 5.2.1.3: 1,5s for elaboration of information received from a BG
In each time frame of 800ms there will be never more than 8 balises detected. Therefore if the system is capable of handling 1 balise per 100ms, the delay will never me more than 800ms – 8*10ms + 1 cycle time of the EVC and 1 cycle time of the BTM. As the minimum time between two detected balises is app. 10ms, it is necessary to be able to store at least 8 Telegrams in an input buffer.

A decision to be taken is the number of radio messages which can be received per cycle. In case of handing over from RBC to RBC, messages can come from two independent sources. Therefore receiving two messages at the same time has to be taken into account. Messages giving a new MA are sent on request of the on-board.
Nevertheless, no maximum number of messages could be defined.
Missing a radio message is not unsafe. Therefore it is sufficient to design on the maximum average number of messages per second. Assuming that a maximum of two messages per second is received (this can be achieved by delaying answers on ack-requests from the RBC with one second), a maximum of 10 messages per second (8 from balises, 2 from radio) can be received. If the calculation cycle is limited to 80 ms, only one message per cycle has to be taken into account. To be able to handle peaks an input buffer for radio messages (e.g. 8) is needed.

Proposed decision: dimension the hardware to enable a cycle time of 80ms. This way the software will always have to analyze maximum one message per cycle in order to meet the timing requirements. BG messages have priority (unless an emergency message is sent by radio), because they also provide new location references.

A lot of functions do not have to be executed every 80ms. For those a schedule can be set up to safe calculation time on the processor.
If a new message is received (and BG information becomes available) this will lead to a peak in processor/load. Therefore the functions which only have to be executed in such a case may be spread out over more than one cycle.
Below the functions described in figure xxx are further detailed.

### Build BG message (block 2)
The purpose of this block is to manage the Telegrams stored by the basic software according to the specification of the API. As decided above, data structures shall be available to store at least 8 Telegrams. To avoid copying data once a BG message is complete (i.e. all Telegrams are received), there should also be space to leave at maximum 8 Telegrams of a complete message in the structure for further analysis.
This estimation is worst case and will only occur if 7 out of 8 balises were detected > 800ms ago, and then another 8 balises are detected in one cydle. This leads to a theoretical maximum of 15 Telegrams.

Figure xxx
“Telegram structure”: Structure in which Telegrams shall be stored by the “bit walker”.
A completed message can during the consistency check and the check on linking, be kept in the same structure.

In the example shown on the left:
- A message is just made available consisting of 5 telegrams stored at position 16, 1,..,4.
  If no message is available the pointers “last Telegram of “delivered BG message” and “First Telegram of delivered message have a special value.
  After elaboration of the message and retrieving the packets (done in the same cycle) the pointers will be reset to this special value
- Since receiving the last Telegram of the delivered message, 3 more (5, 6, 7) Telegrams were detected.

“Pointers”:
- “Oldest received Telegram”: the oldest Telegram stored by the “bit walker” which has not been used in a completed message. If no Telegram is waiting for the completion of a BG-message the “pointer” shall have a special value.
- “Last received Telegram”: the last Telegram stored by the “bit walker”. If no Telegram is waiting for the completion of a BG-message the “pointer” shall have a special value.
If a complete message is to be passed to the application, then the current function (“build BG message”) shall set pointers to the start and end Telegram of this message:
- “First Telegram of delivered message”: Pointer to the first detected Telegram in the message passed.
- “Last Telegram of delivered message”: Pointer to the last detected Telegram in the message passed.
When a message is passed, the current function (“build BG message”) shall set the pointer “oldest received Telegram” to the remaining oldest Telegram in the list.

The bit walker is expected to manage the “pointers” “oldest received Telegram” and “latest received Telegram” if a new Telegram is added to the data structure, i.e.:
- If the data structure was empty before storing the new Telegram, then both pointers are set to the field were the new Telegram is stored (e.g. “1”).
- If the data structure was not empty the Telegram is stored in the next field after “latest received Telegram” (thus to “1” if the previous one was stored in “16”), and to set the “pointer” “latest received Telegram” to the field were the new Telegram is stored.
Further the BTM, basic software or “bit walker” is expected to perform the CRC checking and write the result in the data structure for the concerning Telegram (variable: “Telegram inconsistent”).

Packets in the messages:
In the structure the packets and “pointers” (indexes) to specific packets shall be stored. For every packet type their shall be an index to “point” at where the packet is stored (if any). If a packet is deleted from the structure by “filtering” (block 9), this can simply be done by setting the “pointer” to a default value indicating “no packet stored”. The “pointers” enable efficient elaboration of the information in the prioritized order when managing the internal data structure (see next chapter).
Question: can there be more than one packet of the same type in a message?, if so is the number limited?

RECEIVING BALISES MORE THAN ONCE, e.g. in case of stand still over a BG, or in case of reversing.

It is assumed that the “bit walker” when receiving a new Telegram, will check if there is already a Telegram of the same balise in the “Telegram structure”. If so the new received Telegram shall be written over the earlier received Telegram.
Exception: if the balise is detected during a reverse movement, it will be rejected.

This can only be done in the “bit walker” because a later check would lead to deleting and shifting in the data structure.

Reasoning for using “pointers”
In stead of passing the complete message from one function to another, the pointers indicate where the applicable information can be found to enable elaboration (checks, filtering and managing the data from the packages) by later functions. At the end of the software cycle the fields are available for further Telegrams (i.e. the “pointers” “First Telegram in the delivered message” and “Last Telegram in the delivered message” are reset to the default value “no BG-message available”). This implies that all functions up to the functions managing the received data and updating the “internal data structure” shall be executed in one cycle. Further elaboration may be postponed to a later cycle (taking into account timing restrictions).

The current function (“build BG message”) shall:
- check if all a complete message is available (only one per cycle!), starting with the oldest received Telegram, (i.e. the last balise, that is number “1” or number “n” depending on the direction in which the BG is passed in, of the BG is detected, or >12,5m has been driven since the detection of the previous balise in the group, or a balise belonging to another group is detected).
  If a complete set is found, i.e. all Telegrams indicated in the headers are received and no emergency message is available from the radio, then
- The “pointers” “first telegram of delivered message” and “last telegram of delivered message” are set to “point” at the first and last Telegram in the message. The value of those pointers in an indication for the later functions that the message is ready for elaboration.
  Deleting the message (by later functions) in case of inconsistencies, filtering, copying to the transition buffer or elaboration of the data, can be done by resetting the pointers.
- The pointer “oldest received telegram” is set to the first Telegram received in advance of the “delivered message” if any. If no further Telegrams are stored the “pointers” “oldest received Telegram” and “latest received Telegram” are set to a special value indicating that there are no further Telegrams stored.
- Retrieve the BG information and store it in the above described data structure “BG info” for further use.
- Check the consistency per Telegram, i.e. check if illegal values are used (beware this depends on the baseline version of the Telegram given in “M_version”). If an illegal value is found this shall be written in the variable “Telegram inconsistent”
- Determine the furthest location given in any of the Telegrams, and store the value in the “BG info”

With the process described above the basis software and the application software are always allowed to write in the data structure, as there is no case where they could write at the same position.

### Data structure for received radio messages
Earlier it was decided that data structures shall be allocated to store at least two messages which are not yet elaborated. However more is also allowed and reduces the risk of losing data. Once a message is completely stored in the data structure the basic software shall set a flag that the message may be elaborated. After elaboration the application software shall reset this flag. Further the basic software shall provide a pointer to the first message to be elaborated. Messages shall be stored in the order in which they are received. Below an example for a data structure capable of storing 4 radio messages is given:

figure xxx
Data structure to store not yet elaborated messages. A special value for the pointer is defined for the case no radio messages are available.
Further pointers to the individual packets are required for efficient elaboration later on.

It's the responsibility of the bit walker to keep track on the position where the next message shall be stored and to update the pointer “first message to be elaborated”.

Per packet status information shall be stored by the functions handling the information:
- 1: default, “to be elaborated”
- 2: “rejected”
- 3: “information processed”
- more?

### Check BG message consistency (block 3A)
The consistency of a completed BG messages will be checked, i.e. it is checked if all balises were received (or the missed ones were duplicated), if in one of the Telegrams the flag “inconsistent” is set (see block 2), if the message counter changed (switchable BG). If one of the conditions is not fulfilled then the message is not consistent. If so:
- Delete the message, i.e. information stored in the message header and the telegrams (except the BG identifier) are deleted.
- The BG is not used as an LRBG, i.e. the BG information is not stored (i.e. the data in the data structure “BG-info” is deleted) in the “list of detected BG's” and the linking distance of the next expected BG (if any) is increased with the linking distance of the inconsistent BG (if available).
- An error reaction will be initiated. This reaction is either the “linking reaction” specified in the announcement of the BG or commanding the service brake if no announcement information is available.

The reaction if a message is not consistent is not found clearly in the SRS.
The current function shall further manage information coming from duplicated BG's and error msg's sent from track-side.

Inputs:
- Pointers to the start and the end of the message to be checked
- List of announced BG's
Outputs
- reset of the start and end pointers to the message if the message is rejected
- deletion of BG-info if the BG shall not be used as LRBG (and not be stored in the list of detected BG's)
- “linking reaction”
Functions in detail:
xxxx
Requirements covered with this functional block:
xxxxx

### Check radio message consistency (block 3B)
Question: are the requirements formulated in subset 37 realized in the radio or basic software or is it part of the application? Working assumption: it is not part of the application.

Conditions for execution of the function:
No BG message is available for elaboration

The current function shall check on illegal values in the message and shall check the timing (i.e. no earlier received message has a later reception time stamp). If the information is invalid then the message shall be deleted, i.e. the “pointer” to the message shall be reset.

Inputs:
message including time stamp of the reception

### Checking linking consistency and update the list of ann. BG's (block 4)
The task for this functional block is to update the “list of announced BG's” if a BG is detected or the end of the expectation window is reached, i.e. deleting announced BG's whenever necessary.
Further the function shall pass the BG-messages and pass the necessary information to the function updating the “list of detected BG's”, if they are consistent according to linking rules.

Data structures affected:
- BG message, i.e. access to the data structure containing the pointers to the first and last telegram in the message (after data consistency check)
- BG information (“BG-info”), i.e. information concerning the identity and position of the BG (detected as well as linking and inaccuracies)
- List of announced BG's (from IDS)
- Train Postion I.r.t. the LRBG (from IDS)
- Number of missed BG's (IDS)
- “Linking reaction” (IDS)

The current function shall update the list of announced BG's if:
- The end of the expectation window is reached without detecting balise 1 of the expected BG, and
- if a linked BG is detected
In the latter case the function shall further check if the “BG information” is consistent with “linking information” stored in the “list of announced BG's”.
If not the BG information and BG message shall be deleted and output variable “linking reaction shall be set”. If one or more BG's were missed the “number of missed BG's” shall be incremented by this number.

#### Deleting the expected BG if the end of the expectation window is reached
If the end of the expectation window is reached before detecting “balise 1” (the reference point of the group), taking into account then the BG shall be deleted from the list of announced BG's and the linking reaction shall be executed, in detail:
- Check if the end of the expectation window, i.e. the maximum distance between the train front end and the expected location of the expected BG plus the “location inaccuracy” became negative.
  {STANDARD CALCULATION OF DISTANCE BETWEEN THE TRAIN AND A LOCATION}
- Check if “balise 1” of the expected BG is in the structure of received Telegrams.
- If the end is reached and “balise 1” is not found then:
- Set the flag “linking reaction” according to the linking reaction stored for the expected BG in the “list of announced BG's”
- Delete the BG from the “list of announced BG's”, i.e. increment the “pointer” “expected BG”, in the “list of announced BG's”

#### Check linking consistency and update list of announced BG's if a linked BG is detected
After the consistency of a message has been checked, it shall be checked if the linked BG received is consistent with the information stored in the “list of announced BG's”.

Possible situations in case of detecting a new BG:
the expected BG is detected
1. Inside the expectation window
2. in rear of the expectation window (in advance is not possible as it will be deleted by than)
another linked BG is detected
1. A further announced BG inside the expectation window for that BG.
2. A further announced BG outside it's expectation window
3. The BG is a not announced BG while the “list of announced BG's” is not empty
4. The BG is a not announced BG while the “list of announced BG's” is empty
the detected BG was already detected

Checking if a BG is inside the expectation window shall be done using the minimum announced location minus LOC_ACC and detection accuracy, and using the maximum announced location plus LOC_ACC and the detection accuracy. Further checking the expectation window shall include checking the passing direction.

1.a	Detection of the expected BG in the expectation window without finding the expected BG.
As found in the expectation window linking consistency for the detected BG is confirmed, the linking distance given in the list of announced BG for the expected BG as a location (i.e. distance from the old LRBG) shall be stored in “BG info”.

1.b	Detection of the expected BG in rear of the expectation window
If the expected BG is found in rear of the expectation window (i.e. too early), then the BG information (detection position etc) and the message given by the BG shall be deleted, (i.e. resetting the “pointers” for the start and end Telegram of the message, and setting the flag “linking inconsistency” in the structure “BG info”.

2.a Detecting a further announced BG inside it's expectation window
If the BG found is not the expected but a further announced BG inside it's expectation window, then:
- The “number of missed BG's is incremented with the number of announced BG's skipped.
- xxx

2.b Detecting a further announced BG outside it's expectation window
If the BG found is not the expected but a further announced BG outside it's expectation window, then:
- The “number of missed BG's is incremented with the number of announced BG's skipped plus one (for the now detected BG).
- The “BG-info” status shall be set to “linking inconsistency”

2.c Detecting a not announce BG when the “list of announced BG's” is not empty
xxxx

2.d Detecting a not announce BG when the “list of announced BG's” is empty
xxxx

3. The BG was already detected before
The “BG info” shall be taken into account (so not to be stored in the list of BG's, maybe if the BG is the LRBG the Train Position may be reset.......), but the message shall be used.

### Recalculate the Train Position Reference after a new linked BG is received from filtering (architecture block 5)
If a linked BG is detected and the linking consistency is checked, then the information concerning the BG shall be passed to the function determining the “Train Position” in reference to this new LRBG.

The first function calculates the “Train Position” in reference to the new LRBG (including the calculation of the Dmin_nom-det and Dmax_nom-det), in detail:
- Calculate the minimum and maximum distance between the nominal and the detected position of the new detected LRBG.
- Set the Train Position (seen from the nominal position of the BG) at the moment of detection equal to the minimum and maximum distance between the nominal and the detected position of the BG.
- Estimate the Train Position at the start of the cycle using the time difference between the moment the BG was detected and the time of the start of the cycle.

After this step the BG information shall be stored.

### Store a detected BG(architecture block 6)
If a linked BG is detected and the linking consistency is checked, and the “Train Position” is calculated in reference to this new LRBG, the BG information shall be stored.
The information needed for a BG to be stored shall include:
- NID_BG and NID_C
- a “pointer” to the expected BG in the structure for storing the announced BG's
- The linking distance to the expected BG.
- Dmin_nom-det and Dmax_nom-det.
- xxxx

In detail, storing the information concerning a new linked BG (the new on-board LRBG) consists of the following steps:
- Check if there is a free element (pointed at by “first free element”), i.e. “pointer” “first free element” < “pointer” “most rear BG”
- If not xxxxxxxxxxxxxxxxxx {see “what to do if BG structure is full”}
- Copy information from the element where information concerning the expected BG is stored to the element where the “pointer” “first free element” is referring to: NID_BG, NID_C and linking distance.
- Copy the index where the new expected BG can be found from the element where information concerning the expected BG is stored to the element where the “pointer” “first free element” is referring to. The link to the new expected BG is now made
- Change the “pointer” to the “next linked BG” in the element where information concerning the previous LRBG is stored, from the expected BG to the index of the element where information concerning the new LRBG is stored.
- Change the “pointer” to the “previous linked BG” in the element where the new LRBG is stored to the index where the previous LRBG was stored.
- Change the “pointers” “LRBG” and “Last detected BG” to the index where the new LRBG is stored
- Change the “pointer” “first free element” to the next index (pointing at the next free element).
- Store data in the element where information concerning the new LRBG is stored:
- Set the “pointer” “next linked BG” to the index of the new expected BG
- Store the minimum and maximum distance between the nominal and detected location of the BG in Dmin_nom-det and Dmax_nom-det.
- Store the location where the BG was found in estimated, minimum and maximum distances
- determine and store the passing direction
- Set the indicatior if the BG is linked to “true”
- Set the furthest location to the linking distance to the new expected BG. If there is no new expected BG use a default value > 0 (e.g. 1000m)
- Set Correction distances to “0” (as the BG is the LRBG).
- Recalculate all correction distances for all elements in the list of “detected BG's” using the formulas from “calculating location and train position 0.0.16”

x. Unlinked BG's

Store the data for the unlinked BG in the list of unlinked BG's, and calculate the correction distance for the detected BG. If an unlinked BG is detected then it shall be stored in the structure for detected BG's, i.e.:
- Calculate the minimum and maximum distance between the nominal and the detected position of the new detected LRBG (detection accuracy plus “LOC_ACC”).
- Check if there is a free element (pointed at by “first free element”), i.e. “pointer” “first free element” < “pointer” “most rear BG”
  If not xxxxxxxxxxxxxxxxxx
- Set the “pointer” “last detected BG” to the value of “first free element” and increment the index stored in “first free element” (beware: circular buffer).
- Store data in the element where information concerning the new LRBG is stored:
- Store information concerning the BG received from track-side; NID_BG, NID_C
- Store the minimum and maximum distance between the nominal and detected location of the BG in Dmin_nom-det and Dmax_nom-det.
- determine and store the passing direction
- Store the location where the BG was found in estimated, minimum and maximum distances
- Set the indicatior if the BG is linked to “false”
- Set the furthest location to the linking distance to the new expected BG. If there is no new expected BG use a default value > 0 (e.g. 1000m)
- Calculate and store the Correction distances (will be negative as the BG is found in advance of the LRBG).

### Cyclic train position calculation (block 7)
The consistency of a completed BG messages will be checked, i.e. it is checked if all balises were received

### Link the reference BG to the “list of detected BG's” (block 8)
Xxxxxx

### Mode/Level filtering (block 9)
Mode and level filtering can be done before analyzing the input data, using the requirements from subset 26 paragraph 4.8.
If a level transition (immediate or for a further location) is received then the received information will not be rejected but stored on-board for later evaluation.

After this check:
- Packets are deleted from the data structure containing the message if they shall be rejected according to subset 26 paragraph 4.8 in the current mode and level.
- Packets are deleted from the data structure containing the message and stored in the data structure “transition buffer” if they shall be stored for later use according to subset 26 paragraph 4.8 in the current mode and level.

### Update the list of BG's in case of BG's passed during reversing

# Management of location based data
A lot of information given from ETCS track side to on-board is “Location based”, i.e. the information is valid for a certain location given as a distance from a reference BG. The current function will manage the elaboration of packets containing “Location based data” into the (already available) sorted internal data structures which shall enable efficient further elaboration of the data (e.g. braking curve monitoring, constituting the planning area, etc.).

Description: Elaboration of the packets containing “Location based data” into the (already available) sorted internal data structures.
Inputs:
Packets containing “Location based data” (see below)
Affected data in the “data stored on-board”:
- Internal data structures storing “internal data structures”
- Status of received packets (change to “elaborated”, thus may be forgotten)
Outputs: -

List of types of location based data:
- List of announced BG's
- Movement Authority
- Distance to run in staff responsible mode (comparable to MA in FS).
- Gradient
- static speed profile
- track conditions: change of power supply and change of current consumption

“Location based” data is categorized for the purpose of defining data structures:
- movement authority (MA) list of sections, message 37, packet 12 (level 1), message 3, packet 15 (level 2), 16 (repositioning, i.e. extending the current section), message 33 (??), packet 70 (route suitability), message 9 (request to shorten MA), packet 90 (track ahead free leads to MA request) minimum number of elements to be stored: 6
- list of announced BG's linking information: packet 5 minimum number of elements to be stored: 30
- adhesion factor: packet 71; only one element
- the “gradient profile” (in: pkt 21) minimum number of elements to be stored: 50
- Speed profiles: packet 27 (SSP) {the worst case can be determined at reception}
  Packet 13	minimum number of elements to be stored: 50
- Speed restrictions and non-continuous speed profiles: packet 51 (axle load profile), packet 52 (permitted braking distance), packets 65/66 (TSR), packet 88 (level crossing, incl. stop condition to be reset at standstill).
  minimum number of elements to be stored: TSR: 30, axle load: 30, permitted braking distance: 5 , level crossing: 10.
- Reversing area's: packets 138, 139	minimum number of elements to be stored: 1
- Mode dependent speeds: message 2 and packet 80 minimum number of elements to be stored: 6
- Level transitions: packet 41 minimum number of elements to be stored: (see ss26, 5.10.1.6): 1
- RBC transitions: packet 131
- Radio infill area entry or exit: packet 133
- Loop announcement: packet 134
- DMI information: packets 72,76 (text messages), packet 79 (geographical position information), message 34 (track ahead free request) minimum number of elements to be stored: fixed text: 5, free text: 5, geographical position:
- Track conditions (to be passed to the TIU and displayed at the DMI): packet 39 (traction system), packet 40 (current limitation), packet 68 (diverse track conditions), packet 69 (platform conditions). Pkt 139 minimum number of elements to be stored: 20, + 1 for change power supply + 1 for platform conditions, + 1 for current limitation
- Route suitability: minimum number of elements to be stored: 3
- Big Metal Mass: Technical information (to be used for BG-filtering): packet 67 (ignore BG integrity) minimum number of elements to be stored: 5
- Virtual balise covers: minimum number of elements to be stored: 10
- list of position report locations. In: pkt. 58 minimum number of elements to be stored: 15
- Announced national values. In: pkt 3 minimum number of elements to be stored: 1
  If new national values are announced, then those can lead to more restrictive braking curves. Therefore a speed restriction has to be calculated for the location where the values become valid, based on the targets in advance of this point.

All above information contains “Locations”. These “Locations” can all be managed in the same manner. A location is defined using the following data structure:

For each location the “original reference” (ORBG) and the distance from this ORBG are remembered.
In the data structure for passed BG's a correction distance is stored such that:

Distance between train and location =
Distance from ORBG – Train Position (I.r.t. LRBG) - the stored correction distance (all including tolerances).

A location is thus always stored as a distance from the nominal location of the ORBG (thus not having tolerances). Location based data is given from track-side as a chain of incremental distances. This shall be converted during the elaboration and storage.

Typically location based data has to be available in the order it is passed. This requires ordering and reordering if an element The following situations have to be taken into account:
- some types of location based data are not sent in the order they are passed, i.e. an element can be received which has to be included halfway the list.
- some types of location based data can be withdrawn from the list.
- Some types of location based data can be updated
- Information stored for a location can change, e.g. if the axle load changes, then the speed restrictions stored for this item shall be changed.
- Shifting of data shall be avoided.
Figure X
General data structure for location based data of a specific type: “LOCATION BASED DATA STRUCTURE”
- closest: The element related to the location which is the closest to the train front end
- Furthest: The element related to the location which is the closest to the train front end
- First free: The element where the next received “location based data element of the specific type

Each element shall contain the index of the element where the preceding location is stored, the index of the element where the next further location is stored, the location (see type description above) and fields for information depending of the type of location based data.

figure xx
Generic structure for an element in a data structure for location based data

General functions to be performed on a “LOCATION BASED DATA STRUCTURE” when new information is received are:
- Replace all data from a certain location onwards with the new received information.
- Insert one element in the structure at the right location, i.e. between the last preceding and the first next location of the same type.
- Delete one element of the structure, i.e. restore the order and free the memory where the information was stored.
- Update the information for a specific (already stored) element containing location based data, e.g. update the speed of “axle load dependent speed restrictions” in case the axle load changes.

ORDER IN WHICH PACKETS CONTAINING LOCATION BASED DATA SHALL BE ELABORATED
There are a few requirements determining the order in which different types of data shall be analyzed:
- MA's may only be accepted if a static speed profile and gradient information is available. Therefore the latter ones shall be elaborated before the MA information is elaborated.
- xxxxx

Scope of the function
The current function includes all elaboration of packets containing location based data into the internal data structure for location based data, further elaboration is not included.
MRSP and the list of targets for braking curve monitoring are also location based, but they are a further elaboration of the received data. The building of the MRSP and list of braking curve targets is therefore not handled in the current function but in “Build MRSP + list of targets at the LRBG” (see figure below).

figure xxx

## Location based level transitions
Xxxxx

New information concerning location based level transitions........?

## Linking information
xxxxx

Receiving new linking information:
m) New linking information received as non-infill information shall replace all stored linking information from the LRBG.
n) New linking information received as infill information shall replace all stored linking information from the reference location of the infill information (i.e. the balise group at next main signal).

When new linking information is received for announced, the linking information shall be stored as a location in the data structure for announced BG's (see structure of an announced BG).
Strategy for storing linking information in the proposed data structure per BG:
- Determine which information in the existing “List of announced BG's” shall be kept.
- Delete all information in the structure from the remaining information onwards.
- Linking information for distances in rear of the on-board LRBG shall be stored in the list of detected linked BG's which references in two directions.
  The data structure storing information concerning the LRBG shall refer to the expected BG

## Gradients
Xxxx

Receiving new gradient information:
b) New Gradient Profile information shall replace all stored Gradient Profile information from the start location of the new information.

## Static speed profile
Xxxxx

Receiving new SSP information:
a) New Static Speed Profile information shall replace all stored Static Speed Profile information from the start location of the new information.

## Speed restrictions
xxxxxx

Receiving new speed restrictions:
c) New Axle Load Speed Profile information shall replace all stored Axle Load Speed Profile information from the start location of the first element of the new information.
d) New Speed Restriction to ensure Permitted Braking Distance information shall replace all stored Speed Restriction to ensure Permitted Braking Distance information from the start location of the first element of the new information.

## Movement authority (MA)
Xxxxx

Receiving new MA information (not in par. 3.7):
Complete MA
Infill information

For speed and distance supervision the allowed distance to run shall be clear. This information is given, on request of the on board unit, in pieces which can all have their specific time out values. The parameters defining when an MA shall be requested by the OBU, and the structure to store the MA are part of the internal data structure.

The data structure storing the MA-request parameters shall be able to contain the following information:
- Time repeating the MA request, i.e. an MA shall be requested if the time elapsed since the last MA request reaches this value.
- Time, before reaching the indication point, at which an MA request shall be sent.
- Time, before any MA-timer elapses, at which an MA request shall be sent

The data structure storing the MA shall be able to contain the following information:
- A number of sections with their starting location (i.r.t. the LRBG), a timer stop location and a timer.
- End section information: the length of the end section including the length, an end section timer start location and an end section timer.
- A limit of authority speed plus timer related to this speed (LOA timer)
- A danger point including the related release speed.
- An overlap including overlap timer a start location for the overlap timer and a with the overlap related release speed.

The above data structure shall enable the following functions:
xxxxxxxxxx

A graphical representation of the “MA-structure” is given at the next pages:

Figure xxxx:	TIMER
A timer can be:
- started
- updated (set a new duration)
- ended (time-”starting time” > duration)
- removed

## Adhesion factor
Xxxxxxx

Receiving new information concerning the adhesion:
l) New adhesion factor information shall replace all stored adhesion factor information from the start location of the new information.

## DMI information
Xxxxxxxx

New DMI information (text messages) are added to the existing text messages

## Deleting a BG after the last related “Location” has been passed

Xxxxx

## Train characteristics

## DMI parameters

## Brake system model

## DMI mirror

## Procedure status

## List of BG (SR and SH)

## Mode and level status

## RBC contact status

## STM status

xxxxxxxx

# Building MRSP and list of targets i.r.t. the trains front end
The SSP and speed restrictions in the “location based data” have to be combined to a most restrictive speed profile (MRSP) and list of targets for braking monitoring given as a distance from the LRBG. This is the task of the current function.

Description:
The current function will combine the SSP and the list of speed restrictions (coming from TRS's, most restrictive braking distances, axle load profiles and level crossings) into a most restrictive speed profile (MRSP) and a list of targets subsequently used for braking curve monitoring.
Inputs: SSP and list of speed restrictions (including a mark which SR is not yet included in the MRSP and “list of targets”.
Outputs: MRSP and “list of targets for braking curve monitoring”, given as distances (one value without tolerance) from the front end of the train (taking into account the train length for speed increases if necessary).

The train specific static speed profile and the speed restrictions are used for:
- braking curve monitoring; according to the most restrictive targets
- ceiling speed monitoring: according to the most restrictive speed at a certain location
- displaying the planning area to the driver; most restrictive speed profile in the area ahead.

For displaying to the driver (planning area) and guarding the actual ceiling speed, the maximum speed at any place shall be calculated (MRSP). For braking curve monitoring the actual most restrictive target is sufficient. The latter will not change till it's passed. Therefore a list of targets can be derived which has to guarded one by one, by braking curve monitoring.
In the modes FS (full supervision), OS (on sight) an LS (limited supervision) the MRSP can be derived from the SSP and speed restriction. In shunting and staff responsible (SH and SR) the mode profile can be given in the message commanding the transition to the state.

MRSP
The most restrictive speed profile is giving the lowest speed of the resulting SSP, and the list of speed restrictions. When constructing the MRSP the distance to be taken into account that for speed decreases, is the minimum safe distance from the train fronts end (therefore the maximum “correction distance”) and for speed increases the maximum safe distance from the train fronts end (therefore the minimum “correction distance”). The MRSP is to be used for supervising the actual speed and for displaying at the DMI (planning area).
Update:
- The MRSP has to be calculated every time a new SSP is received and when a new LRBG is detected.
- New speed restrictions can be included in the existing MRSP, without recalculating the complete MRSP. Therefore it's necessary to mark in the “list of speed restrictions” which speed restrictions have not yet been taken into account in the MRSP.
- After every change of the train position (every cycle) the MRSP shall be updated according to the maximum and minimum distance driven (the maximum is relevant for speed decreases, the minimum is relevant for speed increases). This could lead to changing the order of points where the speed increases and points where the speed decreases.

An obvious example is the case with two TSR's at a short distance:
Figure xx
Example with overlapping TSR's due to increasing tolerances. One point (distance from the train front end) shall be removed from the MRSP.

For braking curve monitoring (BCM) only speed decreases are relevant, and only those which do not lead to a higher “braking curve speed” than further targets with a lower target speed (see figure xxxx).

 Most restrictive targets for BCM
For braking curve monitoring the most restrictive target shall be known at every moment. In general a speed decrease in the MRSP is a potential target. But not every speed decrease is a relevant target because they can be above the braking curve to another target ( see figure xxx).

Figure xxx
Example of the selection of the “list of most restrictive targets” which have to be handled by “Braking Curve Monitoring” one by one. In the above example the “green” target will never be “most restrictive” and will thus not be included in the “list of most restrictive braking curve targets”.

When analyzing the MRSP from the furthest location towards the train front end, all relevant speed decreases (most restrictive targets for braking curve monitoring) are found. These locations will be stored (including the speed level) and have to be guarded one by one for braking curve monitoring.

Update:
The list of most restrictive targets shall be recalculated every time the MRSP has changed.

The data structure of the MRSP and list of target is different from the structure for general location based data because all locations are given as a distance from the LRBG only. So the data structure will not be based on the type “Location”.

# Output functions

## Braking curve monitoring
Xx

## DMI control
Xx

## Mode and level management
Xx

Xxxxxx

# Diverse functions

## Assigning passing direction (when given by the RBC)
Xx

Xxxxxx

# Variables

## Movement authority

Aantekeningen:
- The track-side can give several SSP's (for different cants or different train types (freight P, freight G, passenger). At the moment of reception of the SSP, the train can select the worst case values valid for the specific train type. Therefore for each train only one SSP has to be stored. The “borders” (Locations where the speed level changes) are equal for the different speed profiles.
- Question: what's the reason for the difference in structure for special SSP categories and axle load profile?
- Q_trackinit:? What's meant with resuming the initial state of the packet?