INPUT AND OUTPUT DATA

General
Below an overview of the input and output information for the system is given. The information is described in the following sources:
- Trackside: subset 26 chapter 7 and 8. Chapter 6 (baseline 2) has not yet been analysed, however the expectation is that this chapter will not contain more information (only diffferent format)
- TIU: annex of the API specification
- DMI: annex of the API specification
- JRU: not used
- odometer: the API specification

From the available input data the part which is necessary for the demonstration on Amsterdam-Utrecht has been selected. Data only needed for functions which are not realised in this first implementation are marked in grey. Those functions can be added later-on without affecting the core functionality realised in the demonstrator for Amsterdam-Utrecht.

Based on the replacement strategy for the data (a.o. ss26, 3.7.3) data structures will be defined to store the received data and to update the data if new information is received from the same type (sometimes overwrite, sometimes extend, or a combination).

For the output data it is defined which functional blocks shall be the source of the data, and which internal data shall be available to enable the determination of the required outputs.

Most of the input information shall be stored in a way that it can be remembered, updated and maintained (e.g. when driving). Other inputs are always used in the current cycle, have their effect and can be deleted.

Inputs from track-side

nb	Packet Name	Action / process and/or storage	Replacement strategy of existing information / remarks	Resulting data structure
0	Virtual Balise Cover marker	Store in “17”: Marker given in the packet to indicate the BG can be ignored if the marker is stored on-board (see packet 6). / no on board data	Not used on the infrastructure
2	System Version order	Store in “11”, Track data
3	National Values	Store in “10”, national/default data
5	Linking	Store in “1”, location based data: list of announced BG's
6	Virtual Balise Cover order	Store the identity of the balise cover in “11” track data (new packet 6 in addition or replacing?)	Not used on the infrastructure
12	Level 1 Movement Authority	Store in “1”, location based data: MA
13	Staff Responsible distance information from loop	Store in “1” location based data: distance in SR, Store in “1”, location based data: MA	No loops
15	Level 2/3 Movement Authority	Store in “1”, location based data: MA
16	Repositioning Information	Reset of the length of the current section of an MA What is the effect on the other location based data? / Used to update the MA
21	Gradient Profile	Store in “1”, location based data: gradient profile
27	International Static Speed Profile	Store in “1”, location based data: static speed profile
39	Track Condition Change of traction system	Store in “1”, location based data: track conditions	No track conditions
40	Track Condition Change of allowed current consumption	Store in “1”, location based data: track conditions	No track conditions
41	Level Transition Order	If no distance is given but a special value, i.e. an immediate level transition order, then the level available on-board with the highest given priority shall be stored in “6”: the list of direct orders / If a distance is given then store in “1”, location based data: level transition order. / Further for transitions to level 1, level2/3 of SN a “flag” has to be set to indicate to the function “filtering” that a (and which) level transition is announced.
42	Session Management	Store in “13”, procedure management: “establish connection” or “terminate connection”
44	Data used by applications outside the ERTMS/ETCS system.	Store as a complete packet for forwarding to the adpressed STM.	No STM management
45	Session Management	Store in “13”, procedure management: ?????
46	Conditional Level Transition Order	Like immediate order given by pkt 41, unless the current level is given in the priority list. In that case no action and no storage.
49	List of balises for SH Area	Packet given together with the acceptance of shunting. / Store in “8”: List of BG's which may be passed in SH or SR (only one of the modes is active at a time)
51	Axle load Speed Profile	Store in “1”, location based data: speed restrictions
52	Permitted Braking Distance Information	Evaluate the maximum speed based on the permitted braking distance and data stored on-board. / Store in “1”, location based data: speed restrictions
57	Movement Authority Request Parameters	Store in “14” parameters for procedures: MA request
58	Position Report Parameters	Store in “14” parameters for procedures: position report
63	List of Balises in SR Authority	Packet given together with the acceptance of staff responsible. / Store in “8”: List of BG's which may be passed in SH or SR (only one of the modes is active at a time)
64	Inhibition of revocable TSRs from balises in L2/3	Store in “17”: filtering data
65	Temporary Speed Restriction	Store in “1”, location based data: speed restrictions
66	Temporary Speed Restriction Revocation	Update “1”, location based data: speed restrictions
67	Track Condition Big Metal Masses	Store in “1”, location based data: big metal mass	Technical information
68	Track Condition	Store in “1”, location based data: track conditions	No track conditions implemented
69	Track Condition Station Platforms	Store in “1”, location based data: track conditions	No track conditions implemented
70	Route Suitability Data	Store in “1”, location based data: route suitability data
71	Adhesion Factor	Store in “1”, location based data: adhesion factor
72	Packet for sending plain text messages	Store in “1”, location based data: DMI data
76	Packet for sending fixed text messages	Store in “1”, location based data: DMI data
79	Geographical Position Information	Store in “1”, location based data: DMI data
80	Mode profile	Store in “1”, location based data: mode dependent speeds	Replaced at the reception of a new MA (also if no Mode Profile is included), but only beyond the infill reference location.
88	Level crossing information	Store in “1”, location based data: speed restrictions / (including a speed restriction to stop if necessary..	No level crossings at Amsterdam-Utrecht
90	Track Ahead Free up to level 2/3 transition location	Leads to an MA request. / To be used in MA management (“1”)
131	RBC transition order	Store in “1”, location based data: RBC transitions
132	Danger for Shunting information	?????????
133	Radio infill area information	Store in “1”, location based data: Radio infill area	No radio infill foreseen
134	EOLM Packet	Gives the distance to the start of a loop plus further relevant information. / I this information relevant for the LTM, or is the LTM passing any loop information and shall the check been done by the application software. / In the latter case it is location based data: / Store in “1”, location based data: Loop announcement	No loops
135	Stop Shunting on desk opening	Store in “6” direct and conditional orders
136	Infill location reference	To be used in calculating the reference for location based data in the (which?) part of the packet (or telegram?) following this packet 136. / As the reference is in advance of the LRBG, the concerning locations are stored in reference to the LRBG (only if the linking distance is provided) / no data stored
137	Stop if in Staff Responsible	Store in “6” direct and conditional orders
138	Reversing area information	Store in “1”, location based data: reversing area's
139	Reversing supervision information	Store in “1”, location based data: reversing area's / What's the difference between D_reverse and L_reversearea?
140	Train running number from RBC	Store in “9”, train data
141	Default Gradient for Temporary Speed Restriction	Store in “11”, track data
143	Session Management with neighbouring Radio Infill Unit	Store in “13”: procedure status???	No RIU
145	Inhibition of balise group message consistency reaction	Information to be used during consistency checking. This requires an early analysis of the message
180	LSSMA display toggle order	?	No limited supervision
181	Generic LS function marker	?	No limited supervision
254	Default balise, loop or RIU information	Packet used in switchable BG's when track side information is not available. / Shall be taken into account when storing information from the message.
Msg / Id		For all messages / If M_ACK=1 (acknowledgement from the system (?) required), this information shall be stored in “13”: procedure status information
2	SR Authorisation	Store in “6” direct and conditional orders
3	Movement Authority	Contains the MA: see packet 15
6	Recognition of exit from TRIP mode	- no action (acknowledgement see above)
8	Acknowledgement of Train Data	??
9	Request to Shorten MA	Update “1”, location based data: MA's
15	Conditional Emergency Stop	Store in “1”, location based data: conditional emergency stop
16	Unconditional Emergency Stop	Store in “6”: direct and conditional orders.
18	Revocation of Emergency Stop	Update “1” or “6”/”13”, In case of an unconditional em. Stop, revocation during braking is a kind of procedure “braking due to unc. em. Stop number xxxx”, thus stored in “13”
24	General message	-
27	SH refused	stored in “13”: procedure status information
28	SH authorised	stored in “13”: procedure status information
33	MA with shifted reference location	Update “1”, location based data: MA's
34	Track ahead free request	Store in “1”, location based data: DMI information
37	Infill MA	RIU only...........	No RIU
40	Train Rejected	stored in “13”: procedure status information
32	RBC/RIU system version	Store in “11”, Track data
38	Initiation of a communication session	stored in “13”: procedure status information
39	Acknowledgement of termination of a communication session	stored in “13”: procedure status information
41	Train accepted	stored in “13”: procedure status information
43	SoM position report confirmed by RBC	stored in “13”: procedure status information
45	Assignment of coordinate system	Update “3” reference system, i.e. store the direction in which a BG was passed (train orientation at the time of the passage) in the data structure for “passed BG's”)

Outputs to track-side

nb	Packet Name	Action to build the message from the originating data structure / remark	Originating data structure
0	Position Report	Functional block: xxxxxxxxxx / Store the actual distance plus tolerances from the on-board LRBG, the identity of the LRBG and the passing direction in packet 0	“3” train position and reference system (“List of passed BG's”)
1	Position Report based on two balise groups	As above, but add the identity of the previous BG if no passing direction is available	“3” train position and reference system (“List of passed BG's”)
3	Onboard telephone numbers	Functional block: xxxxxxxxxx	“9” train data
4	Error Reporting	Functional block: xxxxxxxxxx	“18” error status
5	Train running number	Functional block: xxxxxxxxxx	“9” train data
9	Level 2/3 transition information	?????
11	Validated train data	Functional block: xxxxxxxxxx	“9”train data
44	Data used by applications outside the ERTMS/ETCS system.	From STM management, / STM management not implemented

Mes. Id.	Message Name	Action to build the message from the originating data structure	Originating data structure
129	Validated Train Data	See above (packets)
130	Request for Shunting	Function “procedure management” will generate the request	“13” procedure management
132	MA Request	Function “MA management” will generate the request	“13” procedure management
136	Train Position Report	See above“7” intermediate analysis results”	“7” intermediate analysis results”
137	Request to shorten MA is granted		“7” intermediate analysis results”
138	Request to shorten MA is rejected	“7” intermediate analysis results”	“7” intermediate analysis results”
146	Acknowledgement	Acknowledgement of a received message, identified by the time stamp in the message. Functional Block: “Radio message consistency” because this function determines if the message is ready for evaluation. Information then stored in “7” intermediate analysis results”	“7” intermediate analysis results”
147	Acknowledgement of Emergency Stop
149	Track Ahead Free Granted
150	End of Mission
153	Radio infill request	No Radio infill
154	No compatible version supported
155	Initiation of a communication session
156	Termination of a communication session
157	SoM Position Report
158	Text message acknowledged by driver
159	Session Established

Inputs from TIU (derived from the API)

Train status (grey text: not needed for Amsterdam-Utrecht demonstrator), API packet 0
- Status of EB, SB, traction cut off; (active, not active, unknown, failed)
- Flag indicating that the TIU is commanding SB, EB or traction cut off (interface between TIU and EVC, not TIU and train)
- ETCS system “Isolated”
- Train controlled from other unit: “Sleeping”
- Tilting on/off, relevant in case of selection of a train specific SSP: “train data”
- Direction controller ( forward, “0”, “backward”)
- Selected cabin: (cab A, none, cab B, failure)
- Train integrity (state: yes/no, in the API a variable for length and/or time is missing!!!!!)
- Vigilance control (state?, external device active?)
What's meant with filtered values

Brake model parameters, API packet 3
xxx { to be filled }

Further (in the API) defined inputs from the TIU, but not needed for Amsterdam-Utrecht demonstration:
Text messages from the train to the ETCS DMI: API packet 1
Test and failure detection: API packet 6
STM specific behavior: API packet 7
Specific from MVB: Alstom application specific, packet 8
Diagnostic information: packet 12
Inhibition level: packet 13.

Outputs to TIU (derived from the API)

Brake and traction commands (EB, SB and TCO): packet 0
- EB command
- SB command
- TCO command
- Vigilance disable order (order to disable train-side (?) vigilance control)

Further (in the API) defined outputs to the TIU, but not needed for Amsterdam-Utrecht demonstration
Track conditions packets 1, 5,
Odometric data, packet 2,
mode and level information, packet 3
Train type, i.e. the type of brake R, P or G, packet 4
Location reference, packet 6
Test and vigilance commands: packet 7
STM state: packet 8
diverse information (train length, train number, level inhibition ????????, data change due to change of running direction????)

What's specified in general for vigilance??

Conclusion: for Amsterdam-Utrecht only the emergency brake, service brake and traction cut of commands are needed as outputs to the TIU.

Inputs from DMI (derived from the API)

Acknowledgement from the driver on information (free text) sent to the DMI earlier: packet 50.
message identifier corresponds to packet 9, packet 68 “EVC_message”
Driver_ack_Level_tr	Boolean	Ackn of level transition
Driver_ack_LS	Boolean	Ackn of Limited Supervision mode
Driver_ack_OS	Boolean	Ackn of On Sight mode
Driver_ack_SH	Boolean	Ackn of Shunting mode
Driver_ack_SR	Boolean	Ackn of Staff Resp. mode
Driver_ack_UN	Boolean	Ackn of Unfitted mode
Driver_ack_RV	Boolean	Ackn of Reversing mode
Driver_ack_SN	Boolean	Ackn of SN mode
Driver_ack_TR	Boolean	Ackn of Train Trip

Acknowledgement from the driver on information (fixed text) sent to the DMI earlier: packet 77.
message identifier corresponds to packet 76 and 78 “Track message”

Operation of a button (for buttons displayed, see packet 5) by the driver: packet 52
Driver_start	Boolean	Start
Driver_req_override	Boolean	Override request
Driver_req_SH	Boolean	Shunting request
Driver_req_continue_SH	Boolean	“Continue Shunting on desk closure” request
Driver_req_exit_SH	Boolean	“Exit of Shunting” request
Driver_req_NL	Boolean	Non Leading request

Data entered by the driver: packet 53 and packet 54 (confirmation). As far as used for level selection at start of mission. A data-entry procedure is not foreseen in the first demonstration.

DMI controlled window exit request: packet 67, needed for the demonstration???

Question box reply: packet 73, only used for track ahead free request (in the current specification)

Question: How is the confirmation on data given with packet 3 returned to the EVC?

Further (in the API) defined inputs to the DMI, but not needed for (first implementation of the) Amsterdam-Utrecht demonstration
- STM error on DMI ????: packet 48.
- Text message deleted (due to full stack): packet 56
- Connection confirmation: packet 57, not needed in a demonstrator (technical information only)
- DMI state: packet 58, used for connection mgt, not needed for the demonstration
- data for the JRU: packet 59: not needed for the demonstration
- Report on-going acknowledgements: packet 70, shouldn't be necessary (what is done with this information in the EVC?)
- Report on deletion due to full stack: packet 79, not needed for the demonstration
- iBox state: packet 85: used in case of a remote connection to the DMI, not needed for the demonstration
- ATP test result, packet 87: no test used for the demonstration
- Results for additional Data-Entry (for STM's): packet 180, not implemented in the demonstration (STM and data-entry)

Outputs to DMI (derived from the API)

Minimum functionality for the demonstration:
- speed dial including braking curve (“hook”)
- planning area: most restrictive speed profile ahead
- text messages (including acknowledgements)
- Level selection at start-up
- acknowledgement of level transitions

Message to delete elements on the DMI: packet 2
It's not clear if this only applies to text messages and acknowledgement requests or to all data? Further for specific data (a.o. text messages) special packets are sent to delete the data from the screen.

Confirmation request: packet 3
Sending text or data fields plus an identifier of the confirmation asked (for data entry?)
How is responded to the EVC after receiving this packet?

Text message with or without confirmation or acknowledgement request: packet 9 + packet 68 in case of required acknowledgement
{One line of free text}

Fixed text message to be displayed (identifier from track to train packet 76): packet 76
Fixed text message to be deleted: packet 78

Displaying and hiding buttons: packet 5
list of buttons is not included in the API (available in the standardised screen layout?, TS50459 )

Sound activation: packet 7
list of sounds is not included in the API (available in the standardised screen layout?, TS50459 )

Speed, braking curve and target: packet 8, packet 43 and packet 71.
New information shall overwrite the existing information.

Display an icon (not, constant, flashing): packet 11
list of icons is not included in the API (available in the standardised screen layout?, TS50459 )
Data for viewing after a driver request: packet 15
list of data is not included in the API

Planning area speed restrictions: packet 19, a translation between speed and width of the indication is needed.

Planning area gradients: packet 26

Planning area displaying on/off: packet 31, in certain modes the planning area shall not be shown at all (also not an empty planning area).

Geographical position information: packet 33

DMI controlled window request: packet 66, needed for the demonstration???

Question box request: packet 72, only used for track ahead free request (in the current specification)

Further (in the API) defined outputs to the DMI, but not needed for (first implementation of the) Amsterdam-Utrecht demonstration
- Screen control packet 4,
- Screen request: packet 6, is used for displaying windows, but the demonstration can work with a standard screen/window
- EVC connection request: packet 16, for the demonstration PC's with addressable screens can be used.
- Local time: packet 17, for the demonstration the displays local time can be used
- Planning area icons: packet 18, for the demonstration elaborating track data is not needed, thus displaying not possible
- data transmission start/stop: packet 20, not needed in case of communication between PC's
- Set speed info: packet 23, no cruise control foreseen for the demonstration
- Data entry related information: packet 27, data freeze: does this mean that the data is confirmed, final and can not be changed by the driver anymore?, if so what's the use? The EVC could simply ignore changes. nice to have, but not essential for the demonstration
- Driver language transmission: packet 30, only needed if translations are made in the EVC. However it seems more efficient to translate “fixed texts” in the DMI instead of in the EVC. According to the evaluation of DMI packet76, the translation is done in the DMI.
- Tunnels stopping area distance: packet 32
- STM specific test request: packet 37, STM not supported in the demonstration.
- STM accessibility packet 47, STM not supported in the demonstration.
- Acknowledgement retention: packet 69, For the demonstration (and further applications) this function shouldn't be necessary
- Manage ATP test: packet 82: test not implemented for the demonstration.
- Request, confirmation, view and echo additional Data-Entry (for STM's): packet 179/181/183/185, not implemented in the demonstration (STM and data-entry)

Input from the odometer (according to the API specification):

Distance
- minimum distance driven since start up
- nominal distance driven since start-up
- maximum distance driven since start-up

Speed
- Safe nominal speed
- Raw nominal speed
- Raw minimum speed
- Raw maximum speed

Motion state: motion/no motion

Motion direction: cabA/cabB

INPUTS AND OUTPUTS FROM PROCEDURES

Below for each procedure as described in chapter 5 of subset026 the necessary input and output data will be described.

Start of Mission

Inputs/updated:
name	reference	description	Structure where the information can be found
	5.4.2.2	Driver ID
	5.4.2.2	ERTMS level + status	“15” system mode and level
	5.4.2.2	RBC ID of the current RBC, i.e. not an RBC announced using packet 131 + status	“11” track data
	5.4.2.2	RBC phone number of the current RBC + status	“11” track data
	5.4.2.2	Train data ?? which data is needed?? + status	“9” Train data
	5.4.2.2	Train running number + status	“9” Train data
	5.4.2.2	Train Position, i.e. LRBG identity and min, est, max, distance from the LRBG / + status	“3” Train position and “4” reference system

	5.4.3.2, S22	The selected national system	??????

		Answers on requests to the driver (see below, to be read from the “data request buffer”)

outputs:
name	reference	description	Target for the information
	5.4.3.2, S1	Request to the driver to enter or validate the driver_ID (depending on the status valid/not valid) / {Result: flag stored in the data request buffer, that the validated driver-id is available in “12” driver data}	DMI management, driver requests
	5.4.3.2, S2	Request to the driver to enter or validate the level (depending on the status valid/not valid) / {Result: flag stored in the data request buffer, that the validated level is available in “15” mode and level}	DMI management, driver requests
	5.4.3.2, S3	Request to the driver if he wants to enter a new network ID (Y/N) / {Result: Y/N stored in the data request buffer}	DMI management, driver requests
	5.4.3.2, S3	Request to the radio to deliver a list of available and allowed networks / {result: a flag ïn the “radio management buffer” that a radio network is available, i.e. an RBC-ID/phone number shall be determined}	Radio management
	5.4.3.2, S3	Request to the driver to choose between: use the last phone number RBC-ID/phone number, use EIRENE short number, enter or validate RBC-ID/phone number. {result: a flag ïn the “driver request buffer” that a validated RBC-ID/phone number is available in the “track data”}	DMI management, driver requests
	5.4.3.2, A29	Fixed (“Radio network connection failed”) list of fixed text messages to be defined) to the driver	DMI management, fixed text messages
	5.4.3.2, S10	Request to the driver to choose between: “shunting”, “non-leading”, “data-entry” / { result to be stored in the driver request buffer }	DMI management, driver requests
	5.4.3.2, S10/S24/A24	Overwrite the current train position with “unknown”	Train position
	5.4.3.2, S12	Flag “start Data-Entry procedure” / {Result: a flag in the data-entry buffer indicating that all train data is stored and validated, when shall this flag be reset?}	Procedure management, Data-Entry procedure
	5.4.3.2, S13	Request to the driver to enter/validate the train running number (depending on the status valid/not valid)	DMI management, driver requests
	5.4.3.2, S11	Flag “sent train data for validation by RBC” / {Result: status of the train data becomes “validated”}	RBC management, sent train data for validation
	5.4.3.2, S20	Request to the driver to select “start” / {Result: Y/N “start” selected by the driver stored in the data request buffer}	DMI management, driver requests
	5.4.3.2, S21	Flag “sent MA request” / {The result will become available as a mode change to SR or an MA allowing FS or OS/LS/SH, i.e. a mode change to one of those modes} / The mode changes shall be mode in mode/level management	Manage location based data, MA-management.
	5.4.3.2, S22	Request to the driver to acknowledge the selected national system / {Result: Y/N “national system acknowledged” by the driver stored in the data request buffer}	DMI management, driver requests
	5.4.3.2, S23	Request to the driver to acknowledge unfitted mode / {Result: Y/N “start in unfitted acknowledged” by the driver stored in the data request buffer} / The mode changes shall be mode in mode/level management, so the result shall be read by mode/level management	DMI management, driver requests
	5.4.3.2, S24	Request to the driver to acknowledge SR mode / {Result: Y/N “start in SR acknowledged” by the driver stored in the data request buffer} / The mode changes shall be mode in mode/level management, so the result shall be read by mode/level management	DMI management, driver requests
	5.4.3.2, S25	Request to the driver to acknowledge OS/LS/SH mode {combined or separate requests?} / {Result: Y/N “start in OS/LS/SH acknowledged” by the driver stored in the data request buffer} / The mode changes shall be mode in mode/level management, so the result shall be read by mode/level management	DMI management, driver requests
	5.4.3.2, A31	Request to the radio to “open a session” (meaning) with the RBC (of which RBC-ID/phone number is validated) / {result: a flag ïn the “radio management buffer” that a “session is opened” or a flag that the “opening has failed” ??????} failing may take some time, for that period a status “pending” shall be available	Radio management
	5.4.3.2, A32	Fixed (“Radio session set up failed”) list of fixed text messages to be defined) to the driver	DMI management, fixed text messages
	5.4.3.2, A33/D33	Flag “report position in connection with SoM” / {result”in case the train position is marked as invalid, the RBC reports if the position can be validated, this result shall be stored in a data structure from RBC management having a value “pending” available for the time the RBC has not yet answered (or answer not timed out) / 2nd possible result: train is accepted or not by the RBC. This result shall also be stored in the data structure for RBC management	RBC management, report train position
	5.4.3.2, A40	Fixed (“Train rejected by the RBC”) list of fixed text messages to be defined) to the driver	DMI management, fixed text messages