WP3 – G1 Paris – St Ouen
Meeting Report

---
AGENDA

---
Introduction
Agenda
Tuesday, Dec 9 Room S_6056
    12h00 – 13h30: lunch time
    13h30 – 17h30 With Jakob and Baseliyos
- Agreement on the objectives for the workshop
- Perimeter of the analysis
Wenesday, Dec 10 Room S_6056
    9h00 – 9h30 : quick presentation of Benjamin Scade Model
    9h30 - 10h00: quick presentation of Christian Document
    10h00 – 10h30: quick presentation of Véronique ch13 analysis

---
Agenda
    Wenesday, Dec 10 Room S_6056
    11h00 – 13h00: technical issues
    13h00 – 14h00: lunch time
    14h00 – 18h00: technical issues
    Thursday, Dec 11 Room S_3227
    9h00 – 12h00: definition and sharing of homework
    12h00 – 13h00: lunch time

---
Technical part
Braking curves principles

---
3 types of Speed Monitoring
Ceiling
CSM
Target
TSM
Release
RSM
Target
EOA
CSM: Ceiling Speed Monitoring => speed constant limit
TSM: Target Speed Monitoring => speed reduction to a target limit (0 km/h or not)
RSM: Release Speed Monitoring => fixed and constant speed limit used to approach the EOA

---
Braking curve equation
Distance
Vitesse
Vx2 – Vo2 = 2 . A. x
=> parabola

---
Braking curves deceleration
V2
V1
Deceleration is not constant. For ERTMS, it is defined step by step.
In this exemple (black curve), 3 deceleration values are used: red curve up to V2,
blue one from V1 to V2 and yellow curve under V1

---
Target: EOA - DP
CSM
SB
Emergency
Brake
EB
Full service
Brake
TSM
RSM
DP
EOA
EOA is protected by the full (100%) service brake
Danger Point is protected by the emergency brake
There is one EOA/DP couple max in a MA

---
Target: MRSP
V1
CSM
CSM
EB
TSM
V3
CSM
V2
Target
MRSP is the most restrictive speed between the speed limits (SSP, TSR, train max
Speed,...). It is possible to have differents MRSP targets in a MA

---
Target SM: EOA + DP + MRSP
V1
CSM
SB
CSM
EB
TSM
V3
EB
V2
EOA
DP
Each target has to be taken in account to find the braking limits

---
Target SM : EOA + DP + MRSP
V1
CSM
CSM
EBD
V3
EBD
EBI
V2
EBI
SBI
SBD
DP
EOA
There is a delay between the command and the full application of the brake
Therefore intervention curves has to be defined (EBI, SBI) in order to take in
account this delay

---
TSM : EOA + DP + MRSP
V1
CSM
CSM
V3
EBD
FLOI
V2
EBI
SBD
DP
EOA
The most restrictive limit defines the braking intervention : it is the FLOI (First Line Of
Intervention)
FLOI is the reference to define W(arning) curve, P(ermitted) curve and I(ndication) curves

---
CSM Limits
Speed
EBI Limit
dV_ebi
SBI Limit
W(arning) Limit
dV_sbi
dV_Warning
V_MRSP = P(ermitted) Limit
Distance

---
WP3 - G1
Analysis and modeling steps

---
Session details 4:WP3/WP4 coordination  (Day3)
G1 analysis and modeling steps
Step 1 (end of january – beginning of february)
EBD / EBI curves in TSM, CSM and RSM
- only one danger point
- one given MRSP curve with 3 or 4 steps and at least 2 targets
- 3 A_safe constant values (0-50 / 50-100 / > 100 km/h)
- V_release = constant
- Build up times = constants
- no GUI, no SBD
- commands: Emergency Brake and TCO
- display: speed target, distance target, supervision mode (TSM, CSM, RSM), estimated speed

---
G1 analysis and modeling steps
Step 2 (march → first demonstrator)
SBD / SBI1 – SBI2 – FLOI – W – P – I curves
- Add EOA with SBD curve
- command: Service Brake
- matching DMI

---
G1 analysis and modeling steps
Step 3 (june)
Deceleration and build-up times calculation
- gradient
- slippery rail
- matching DMI
Step 4 (if needed)
Options
Calculate V_release
Calculate GUI
LOA, SR limit, specific MRSP

---
Meeting report

---
Done
Before the workshop:
1. Scade model of Speed monitoring changes
2. Scade model of Internal CSM changes
3. Analysis of ch13 with eFFBD model and traceability
4. Description of the functionalities
During the workshop
1. Definition of the technical perimeter of the internal model
2. Definition of our internal steps and milestones
3. Definition of the perimeter of each internal step
4. Definition of the inputs needed for each step

---
Technical assumptions
1. If there is an EB command, an SB command is automatically sent to the train
2. A command is applied at each cycle since its revocation
3. The model does not check if the driver revokes the Emergency Brake as the
train is not at standstill: it is the work of the TIU simulation

---
Question
Is the emergency brake command sent by the mode module in case
of train trip ?

---
Definition of the database
The database shall contain located track events, sorted according to location
Events are for example :
- location of EOA
- location DP
- Change of SSP (location and speed)
- Beginning / end of slippery rail section
- Beginning / end of TSR
- ...
If possible, the location of each event shall be the absolute location, i.e.
refered to the initialisation position of the train.
For each event, the database shall indicate :
- location
- type of event
- train running direction (normal / reverse)
- data: speed or other

---
Location of the target
Target
d1
d2
d3
Location box will send d3 if possible

---
Database information needed for steps 1 and 2
Database information needed for step 1 and 2 are :
- EOA (location)
- DP (location)
- MRSP changes (location and speed)
Database information needed for step 3 are :
- gradient
- adhesion factor

---
To be done
Extract from Scade model (state charts) on the Github => Benjamin
OpenETCS_SCADE_V2.docx on the Github => Christian
W3-G1 working steps document on Github => Véronique
Html eFFBD model on the Github => Véronique
List of external input needed (extract of the eFFBD model) on Github => Veronique
ADD G1 first version on Github => Véronique