WP3 – G1 Paris – St Ouen
Working steps

---
WP3 - G1
Analysis and modeling steps

---
Session details 4:WP3/WP4 coordination  (Day3)
G1 analysis and modeling steps
Step 1 (end of january – beginning of february)
EBD / EBI curves in TSM, CSM and RSM
- only one danger point
- one given MRSP curve with 3 or 4 steps and at least 2 targets
- 3 A_safe constant values (0-50 / 50-100 / > 100 km/h)
- V_release = constant
- Build up times = constants
- no GUI, no SBD
- commands: Emergency Brake and TCO
- display: speed target, distance target, supervision mode (TSM, CSM, RSM), estimated speed

---
Step 2 (march → first demonstrator)
SBD / SBI1 – SBI2 – FLOI – W – P – I curves
- Add EOA with SBD curve
- command: Service Brake
- matching DMI

---
Step 3 (june)
Deceleration and build-up times calculation
- gradient
- slippery rail
- matching DMI
Step 4 (if needed)
Options
Calculate V_release
Calculate GUI
LOA, SR limit, specific MRSP